## Slide 1: Chapter 16
Phone networks

## Slide 2: Introduction
Earliest communication network
Still one of the most important communication networks
Called plain old telephone service - POTS
Served as platform for modems in 1990’s
Best understood as analog information transmission system

## Slide 3: Phone adoption

## Slide 4: Components
Local loop
End office/ central office
Carrier

## Slide 5: Phone network components

## Slide 6: Significant recent developments
Antitrust lawsuit against AT&T in 1974 - 82
  Competitors emerging in long distance service
  Modified final judgment

## Slide 7: 7 RBOCs after Jan 1, 1984

## Slide 8: Telecommunications act 1996
First major overhaul of telecommunications law since 1934
RBOCs allowed to offer long distance service
RBOCs required to allow competitors to use their networks to compete against them

## Slide 9: Phone signals and DSL
300 - 3,400 Hz band for voice channel
25,875 – 138,000 Hz band for upstream data
138,000 – 1,104,000 Hz band for downstream data
High frequency DSL signals can only be carried over short distances

## Slide 10: Phone line channels with DSL
Chart: Frequency

## Slide 11: Cell phones
Popular development in voice communication in first decade of 21st century
~1 cell phone per person in developed world
~1 cell phone per family in developing world
In developing countries, cell phone infrastructure can be cheaper to create than landline infrastructure
  Operating a cell phone can be a business

## Slide 12: Cell phone adoption

## Slide 13: Cell phone technology evolution
First generation (1G)
  Deployment began around 1980
  Voice modulated for transmission using FM
  No data service
  Phones heavy and unwieldy

## Slide 14: Cell phone technology evolution
Second generation (2G)
  Deployment began around 1990
  Digital signals
  Supported both voice and data

## Slide 15: Cell phone technology evolution
3G
  Defined in 2000 as IMT – 2000
  Data rates adequate to support rich multi-media applications, replicating desktop experience
  Minimum data rates specified

## Slide 16: Cell phone technology evolution
4G
Key requirements

## Slide 17: Cell phone technology evolution
Evolutionary developments
  Intermediate system (IS)
  2.5G
  2.75G

## Slide 18: Cell phone technology evolution

## Slide 19: Cell phone architecture

## Slide 20: Cell frequency reuse

## Slide 21: Cell frequency reuse

## Slide 22: Cell towers example

## Slide 23: Code division multiple access
Preferred multiplexing technology for 3G
Any number of chipping codes may be generated
Receiver processes signal in medium with same chipping code

## Slide 24: Summary
Phone system used for personal and business communication for over a century
Landline PSTN phones
DSL service over land line phones
Modified final judgment ’84; Telecom Act ’96
Cell phones
Frequency reuse
CDMA

## Slide 25: Case study – Africa
Celtel
Yet
Stated opportunity

## Slide 26: Hands-on exercise
CDMA
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40
Chipped data | -1 | 1 | 1 | -1 | -1 | 1 | 1 | -1 | -1 | 1 | 1 | -1 | -1 | 1 | 1 | -1 | 1 | -1 | -1 | 1 | 1 | -1 | -1 | 1 | 1 | -1 | -1 | 1 | 1 | -1 | -1 | 1 | -1 | 1 | 1 | -1 | -1 | 1 | 1 | -1
data | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 27: IT infrastructure design exercise
Voice over IP
  Advantages and disadvantages over traditional phone lines