## Slide 1: Chapter 3
Data Link Layer
With special focus on Ethernet

## Slide 2: Contents
Functions of the data-link layer
Ethernet overview
CSMA/ CD
Error detection and correction
Ethernet frame structure
Switches

## Slide 3: Functions of the Data-Link layer
ATIS Telecom glossary 2007
Ethernet is the most common end-user implementation of the data-link layer

## Slide 4: Data links in typical network

## Slide 5: Ethernet
Most common data link layer technology for end users
Easily understood
Patented in 1977
Ethernet is a low-cost, high-speed communication technology for small networks
An Ethernet network can be up to 100 meters in radius and have up to 250 devices

## Slide 6: Early Ethernet vision

## Slide 7: Early Ethernet diagram (Robert M. Metcalfe and Dave R. Boggs (1976))

## Slide 8: Metcalfe-Boggs transceiver

## Slide 9: Ethernet operation
A typical end-user network looks like this:

## Slide 10: Packet in the medium

## Slide 11: Ethernet data transmission
When PC A wants to send data to PC B, it first adds B’s address before the data
The packet is then sent into the medium

## Slide 12: Broadcast in Ethernet
  Signal is transmitted to all stations connected to the wire
Note that the receipt process is different from the mail system

## Slide 13: Packet receipt in Ethernet

## Slide 14: Role of destination address
If the frame is sent to all computers, why should PC A add B’s address to the frame?

## Slide 15: Ethernet data reception
In broadcast, the network does not direct the packet to its correct destination
  Instead, the packet is simply sent to every computer on the network

## Slide 16: CSMA/ CD - collision
What if multiple senders want to send data at the same time?
The outcome is called a collision
The solution to this problem is called
  Carrier Sense Multiple Access with Collision Detection (CSMA/ CD)

## Slide 17: CSMA/ CD - collision

## Slide 18: CSMA/ CD esentials
Senders send only when they sense that the medium is silent
Continue to listen while sending data
If a collision is detected, stop immediately

## Slide 19: Alternatives to CSMA/ CD
If we did not want to use CSMA/ CD, what could we do
Note that all these methods require co-ordination among computers

## Slide 20: Advantages and disadvantages of CSMA/ CD
Advantages
  Very simple to implement, therefore inexpensive and fast
Disadvantages
  Not scalable due to broadcasting
  Network may not be available when needed

## Slide 21: Error detection
As the packet moves from source to destination, it can get errors
Errors are caused due to the imperfections of the physical world
These errors have to be detected

## Slide 22: Error correction in human communication
Some human error-correction techniques
  Receiver reads back on telephone
  Redundant data
  Sender contact information

## Slide 23: Error correction in computer communication
The general approach to error detection in human communications is not effective in computer communications because of possible error cancellations

## Slide 24: Error correction in computer communication
The general approach to error detection in data communications is to add some meta-data to the original data
Accept if results match, reject otherwise

## Slide 25: Error correction – simple example
Say we want to send HELLO
  We could code it (in decimal) as 8 5 12 12 15 (location in the alphabet)
  A simple meta-data would be to add all the digits till you get a single digit
  8 + 5 + 12 + 12 + 15 = 52
  5 + 2 = 7
  Send 8 5 12 12 15 7

## Slide 26: Error correction problems
If everything goes well, the receiver will get
  8 5 12 12 15 7
    It knows that the 7 is the meta-data
    It calculates 8 + 5 + 12 + 12 + 15 = 52
    5 + 2 = 7
    Hence, data was received without error
But this scheme is too naïve
  What if we receive 8 5 11 13 15 7
  Or 2 2 11 13 15 7

## Slide 27: Cyclic redundancy check (CRC)
Obviously, we need a technique that is more reliable
  Most commercial data communication technologies use CRC

## Slide 28: CRC-32 capabilities
CRC-32 can detect all errors affecting less than 33 (n + 1) bits
CRC can detect all errors affecting odd number of bits
CRC-32 can reasonably reliably detect errors affecting more than 33 (n + 1) bits

## Slide 29: CRC sender procedure
Step 1: User data is dividend, technology specifies a divisor with n + 1 bits
Step 2: At sender, add n zeros to the end of the data (divisor has n+1 bits)
Step 3: At sender, perform modulo-2 division of appended data with divisor
Step 4: At sender, append remainder to data as CRC and send to receiver

## Slide 30: CRC receiver procedure
Step 5: At receiver, perform modulo-2 division of appended data with same divisor
Step 6: At receiver, if remainder is 0, accept data. Else reject data
CRC example follows
  Data: 101010
  Divisor: 1101

## Slide 31: Modulo-2 division rules
Modulo-2 division uses Exclusive OR for subtraction operations during division
0 – 0 = 0
0 – 1 = 1
1 – 0 = 1
1 – 1 = 0

## Slide 32: CRC – Sender operation
 |  |  |  |  |  |  | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
 |  |  |  | 1 | 1 | 0 | 1 | ⁞ | ⁞ | ⁞ | ⁞ | ⁞
 |  |  |  |  | 1 | 1 | 1 | 1 | ⁞ | ⁞ | ⁞ | ⁞
 |  |  |  |  | 1 | 1 | 0 | 1 | ⁞ | ⁞ | ⁞ | ⁞
 |  |  |  |  |  |  | 1 | 0 | 0 | 0 | ⁞ | ⁞
 |  |  |  |  |  |  | 1 | 1 | 0 | 1 | ⁞ | ⁞
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | ⁞
 |  |  |  |  |  |  |  | 1 | 1 | 0 | 1 | ⁞
 |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0
 |  |  |  |  |  |  |  |  | 1 | 1 | 0 | 1
 |  |  |  |  |  |  |  |  |  | 0 | 1 | 1
CRC remainder
Divisor
0’s appended
User data

## Slide 33: CRC – Receiver operation
 |  |  |  |  |  |  | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
 |  |  |  | 1 | 1 | 0 | 1 | ⁞ | ⁞ | ⁞ | ⁞ | ⁞
 |  |  |  |  | 1 | 1 | 1 | 1 | ⁞ | ⁞ | ⁞ | ⁞
 |  |  |  |  | 1 | 1 | 0 | 1 | ⁞ | ⁞ | ⁞ | ⁞
 |  |  |  |  |  |  | 1 | 0 | 0 | 0 | ⁞ | ⁞
 |  |  |  |  |  |  | 1 | 1 | 0 | 1 | ⁞ | ⁞
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 1 | ⁞
 |  |  |  |  |  |  |  | 1 | 1 | 0 | 1 | ⁞
 |  |  |  |  |  |  |  |  | 1 | 1 | 0 | 1
 |  |  |  |  |  |  |  |  | 1 | 1 | 0 | 1
 |  |  |  |  |  |  |  |  |  | 0 | 0 | 0
Remainder is 0
Divisor
CRC from sender
Data from sender

## Slide 34: Ethernet frames with CRC

## Slide 35: Ethernet frame structure
Previous sections show destination address and CRC fields in Ethernet
Other information also necessary
Source for Ethernet standards:
  http://standards.ieee.org/getieee802/portfolio.html

## Slide 36: Ethernet frame structure

## Slide 37: Ethernet fields
Preamble: Allows receiver to synchronize with sender
  10101010 10101010 10101010 10101010 10101010 10101010 10101010
Start Frame Delimiter: Indicates start of frame

## Slide 38: Ethernet fields
Address
  48 bits in length
  All 1’s in the destination address is pre-defined to be the broadcast address on the LAN
  Addresses may be universally administered
    Assigned by manufacturer
    http://standards.ieee.org/faqs/OUI.html
  Or locally administered

## Slide 39: Ethernet address representation

## Slide 40: Ethernet address
Address

## Slide 41: Ethernet address representation
Hexadecimal notation
Bits | Hex | Bits | Hex | Bits | Hex | Bits | Hex
0000 | 0 | 0100 | 4 | 1000 | 8 | 1100 | c
0001 | 1 | 0101 | 5 | 1001 | 9 | 1101 | d
0010 | 2 | 0110 | 6 | 1010 | a | 1110 | e
0011 | 3 | 0111 | 7 | 1011 | b | 1111 | F

## Slide 42: Ethernet address representation
Example
0000 0000 0001 0101 1100 0101 0101 0111 0001 1101 0001 1010
---- ---- ---- ---- ---- ---- ---- ---- ---- ---- ---- ----
0 0 1 5 c 5 5 7 1 d 1 a
Note: Globally unique

## Slide 43: Ethernet fields
Length
  If less than 1,518 (max allowed packet length)
  If greater than or equal to 1,518
Data
  IP packet

## Slide 44: Ethernet fields
Frame check sequence (FCS)
  32 bit CRC value
  Generator polynomial (divisor) specified as
    10000010 01100000 10001110 110110111

## Slide 45: Switched Ethernet - state of the market
Hubs vs. switches
  Hubs send data out to all computers
  Switches only send the data to the intended destination

## Slide 46: Spanning tree protocol
Ethernet vulnerability
  Loops
  Frames forwarded to other switches
  Can disable network
Also, loops are useful
Spanning tree protocol prevents loops

## Slide 47: Spanning tree protocol (contd.)
Builds a loop-free topology on the network
Algorithm
  Switches on the network elect one switch as the root switch
  Each switch
  This eliminates loops and broadcast storms

## Slide 48: Other issues
Ethernet packets are called Frames because they have the synchronization bits at the beginning
Ethernet is commonly available at speeds of 10/100/1000 Mbps, called 10BaseT, 100BaseT or 1GbE

## Slide 49: From Ethernet to the outside world

## Slide 50: Next chapter
Ethernet can reliably send data between computers on one network
To get bigger networks, we connect networks together
The network layer figures out how to find the correct path from source to destination through these networks

## Slide 51: Summary
Why broadcast?
Why CSMA/ CD?
Why CRC?
Why Switches over hubs?

## Slide 52: Example case – Monitoring
4d’s of modern industry
  Dull, distant, dirty, dangerous
IT infrastructure helps service these conditions
E.g. Agriculture
  Monitor soil conditions
  Monitor fertilizer level
  Modify planting density
E.g. Manufacturing
  Trouble-shoot problems

## Slide 53: Hands-on exercise
Ipconfig
Physical address
Converting MAC addresses to binary
OUI lookup

## Slide 54: IT infrastructure design exercise
Ethernet diagrams