## Slide 1: Chapter 8
Routing

## Slide 2: Contents
Definition
Differences from switching
Autonomous systems
Routing tables
Viewing routes
Routing protocols
Route aggregation

## Slide 3: Routing
Definition
In LANs, the source and destination are in the same network
Routing is done by devices called Routers

## Slide 4: Switching vs. Routing
There can be multiple paths between source and destination in larger networks (routed networks)
One of the most important tasks of a router is to send packets to the destination using the best available path

## Slide 5: Switching vs. Routing

## Slide 6: Routers in networks - ISPs

## Slide 7: Routers in networks - homes

## Slide 8: Autonomous systems
Autonomous Systems (AS) are the unit of Internet routing
RFC 1930
  An AS is a connected group of one or more IP prefixes which has a SINGLE and CLEARLY DEFINED routing policy
  Each AS has a globally unique AS number
  Routes are advertised as a chain of AS

## Slide 9: View autonomous systems
BGPlay
AS number to name mapping
  http://www.cidr-report.org/as2.0/autnums.html
    Search for a specific AS. E.g. 5661 (USF)

## Slide 10: AS around 131.247.0.0/16

## Slide 11: Visualizing network routes
https://stat.ripe.net/special/bgplay
http://www.arin.net
  Maintains a database of ownership of IP address blocks
    E.g. Search for

## Slide 12: Routing tables
For each known path to a destination, the router records the next hop in routing table
A router is only responsible for sending the packet to the next router
When multiple paths are known, the metric and next hop associated with each path is recorded

## Slide 13: Example routes to 131.247.0.0/16
Uncompressed and extracted from
  http://archive.routeviews.org/oix-route-views/2009.08/
Network Next Hop Metric Path
131.247.0.0/16 64.71.255.61 0 0 812 174 5661 5661 i
131.247.0.0/16 66.185.128.1 563 0 1668 174 5661 5661 i
131.247.0.0/16 217.75.96.60 0 0 16150 3549 174 5661 5661 i
131.247.0.0/16 208.51.134.246 13186 0 3549 174 5661 5661 i
131.247.0.0/16 12.0.1.63 0 0 7018 174 5661 5661 i
131.247.0.0/16 67.17.82.114 2503 0 3549 174 5661 5661 i
131.247.0.0/16 192.203.116.253 0 0 22388 11537 11096 11096 5661 i
131.247.0.0/16 203.181.248.168 0 0 7660 22388 11537 11096 11096 5661 i
131.247.0.0/16 64.57.28.241 1045 0 11537 11096 11096 5661 i
131.247.0.0/16 216.18.31.102 0 0 6539 11164 11096 5661 i
131.247.0.0/16 216.218.252.164 0 0 6939 11096 5661 i

## Slide 14: Route selection
Routers keep information on all announced routes
  Routers need a measure to compare alternate paths to the same destination
  These measures are called routing metrics
  When alternate paths are available, path with the lowest metric is chosen

## Slide 15: Viewing routes
Many utilities are available to see Internet routes
  Easiest to use is tracert
  In Windows, Start > Run > cmd
  tracert <domain>
USF
Cogent
Sprint

## Slide 16: Routing protocols
There are two kinds of routing protocols used on the Internet
  Exterior routing protocols
  Interior routing protocols

## Slide 17: Simplifying Routing Tables
As more and more organizations join the Internet, routing tables keep getting larger to accommodate the newer routes
Route aggregation is used to simplify routing tables
  RFC 1518 for address allocation with CIDR

## Slide 18: Route aggregation in CIDR
CIDR also includes route aggregation
  Instead of assigning address blocks to end-user organizations, assign larger blocks of addresses to large network service providers
  Organizations acquire addresses from these network service providers
  Routers in the rest of the world only maintain one entry to the ISP’s larger address block

## Slide 19: Routing table without aggregation

## Slide 20: Routing table with aggregation

## Slide 21: Routing table aggregation

## Slide 22: Route aggregation status
http://www.cidr-report.org/
  http://www.cidr-report.org/as2.0/#General_Status
    Route aggregation status
      Networks added to routing table
      Networks that should consolidate
      ISPs decreasing announced routes
      ISPs increasing announced routes

## Slide 23: MPLS
Multi-protocol label switching
Defined in RFC 3031 in 2001
Not a different kind of WAN, but simplifies network layer equipment on any WAN
From RFC 3031:

## Slide 24: MPLS
Consider 2 packets traveling from Lansing to San Diego
But, in traditional routing, each router on the path will independently make a routing decision on each packet

## Slide 25: Networks around sandiego.edu

## Slide 26: MPLS
Packets to be treated similarly are said to be in the same forwarding equivalence class (FEC)
When the 2 packets enter a network, both packets will be assigned the same FEC
FEC is called the label and is added to packet
Routers determine next hop from the label

## Slide 27: MPLS
In MPLS, routers only know how to forward incoming packets with a known set of labels
MPLS simplifies routing in 2 ways

## Slide 28: Software defined networking
Centralize the maintenance of routing tables in a network

## Slide 29: Summary
How routing is different from switching
How routers interface between networks
What are autonomous systems
How routers select routes for packets
What do routing tables look like
What is route aggregation
What is MPLS

## Slide 30: Case study – network resilience following Katrina and 9/11
The superior reliability of packet networks was demonstrated after Hurricane Katrina and 9/11
But effects can be widespread
CNN web page fit on one IP packet

## Slide 31: Hands-on exercise
Bgplay
  Obtain school IP address using tracert
  Obtain CIDR address block from ARIN
  View network neighborhood using bgplay

## Slide 32: IT infrastructure design exercise
Failover