## Slide 1: Chapter 9
Subnetting - Organizing IP addresses within a network

## Slide 2: Contents
Motivation for subnetting
IP address partition with subnetting
Subnetting example
Subnet masks
Subnet computations

## Slide 3: Why subnetting?
Help organize IP addresses within networks and organizations
Registries allocate large address blocks

## Slide 4: Why subnetting?
Subnetting allows organizations to distribute total pool of IP addresses in subnets in different ways
For example, an organization with a /16 address may have

## Slide 5: IP address allocation without subnetting

## Slide 6: IP address allocation with subnetting

## Slide 7: Subnetting and network structure

## Slide 8: Subnetting and network structure
Each Ethernet is given a unique subnetwork ID
  Enables broadcasting within the Ethernet
  Each computer on the Ethernet must be part of this network
Subnetting enables the partition of a large address pool into multiple smaller blocks

## Slide 9: 2-part interpretation of IP addresses

## Slide 10: 3-part interpretation of IP addresses

## Slide 11: Comparing phone numbers and subnetting
Subnetting organizes IP addresses like phone numbers
Only difference is that phone numbers have a fixed structure:

## Slide 12: Subnetting example
Consider an organization with a /16 network address block (131.247.0.0/ 16)
  Most medium-large organizations fall in this category
  Also, most State Universities
    Hence used in the example
  Say, after analysis, the organization settles on 5-bit subnet IDs

## Slide 13: Example with 5-bit subnet IDs
Subnet ID | Campus unit | Subnet ID | Campus unit | Subnet ID | Campus unit
00001 (1) | College 1 | 00010 (2) | College 2 | 00011 (3) | College 3
00100 (4) | College 4 | 00101 (5) | College 5 | 00110 (6) | College 6
00111 (7) | College 7 | 01000 (8) | College 8 | 01001 (9) | College 9
01010 (10) | College 10 | 01011 (11) | <future college> | 01100 (12) | <future college>
01101 (13) | Dorm 1 | 01110 (14) | Dorm 2 | 01111 (15) | <future dorm>
10000 (16) | <future dorm> | 10001 (17) | Branch campus 1 | 10010 (18) | Branch campus 2
10011 (19) | <future branch campus > | 10100 (20) | Administration | 10101 (21) | Campus IT
10110 (22) | <future expansion> | 10111 (23) | <future expansion> | 11000 (24) | <future expansion>
11001 (25) | <future expansion> | 11010 (26) | <future expansion> | 11011 (27) | <future expansion>
11100 (28) | <future expansion> | 11101 (29) | <future expansion> | 11110 (30) | <future expansion>

## Slide 14: Network ID + subnet ID for colleges in example
Campus unit | Subnet ID | First 2 parts of IP addresses by college
College 1 | 00001 | 10000011.11110111.00001_ _ _ . _ _ _ _ _ _ _ _
College 2 | 00010 | 10000011.11110111.00010 _ _ _ . _ _ _ _ _ _ _ _
College 3 | 00011 | 10000011.11110111.00011 _ _ _ . _ _ _ _ _ _ _ _
College 4 | 00100 | 10000011.11110111.00100 _ _ _ . _ _ _ _ _ _ _ _
College 5 | 00101 | 10000011.11110111.00101 _ _ _ . _ _ _ _ _ _ _ _
College 6 | 00110 | 10000011.11110111.00110 _ _ _ . _ _ _ _ _ _ _ _
College 7 | 00111 | 10000011.11110111.00111 _ _ _ . _ _ _ _ _ _ _ _
College 8 | 01000 | 10000011.11110111.01000 _ _ _ . _ _ _ _ _ _ _ _
College 9 | 01001 | 10000011.11110111.01001 _ _ _ . _ _ _ _ _ _ _ _
College 10 | 01010 | 10000011.11110111.01010 _ _ _ . _ _ _ _ _ _ _ _

## Slide 15: Complete subnet addresses for colleges in example
Campus unit | Subnet address (binary) | Subnet address (decimal)
College 1 | 10000011.11110111.00001000.00000000 | 131.247.8.0/ 21
College 2 | 10000011.11110111.00010000.00000000 | 131.247.16.0/ 21
College 3 | 10000011.11110111.00011000.00000000 | 131.247.24.0/ 21
College 4 | 10000011.11110111.00100000.00000000 | 131.247.32.0/ 21
College 5 | 10000011.11110111.00101000.00000000 | 131.247.40.0/ 21
College 6 | 10000011.11110111.00110000.00000000 | 131.247.48.0/ 21
College 7 | 10000011.11110111.00111000.00000000 | 131.247.56.0/ 21
College 8 | 10000011.11110111.01000000.00000000 | 131.247.64.0/ 21
College 9 | 10000011.11110111.01001000.00000000 | 131.247.72.0/ 21
College 10 | 10000011.11110111.01010000.00000000 | 131.247.80.0/ 21

## Slide 16: Example locations of college subnets

## Slide 17: Subnet masks
Subnet IDs are organization-specific
How do hosts and routers know the location of network ID + subnet ID?
Done using subnet masks

## Slide 18: Subnet masks
Sequence of 1’s followed by sequence of 0’s
1’s indicate network ID and subnet ID bits
0’s indicate host ID bits
Subnet mask example: 11111111.11111111.11111000.00000000

## Slide 19: Subnet mask operation
What does a subnet mask do?
For example, consider IP addresses of hosts in 2 colleges, viewed through the subnet mask

## Slide 20: Subnet mask operation
 | Host 1 | Host 2
Destination IP address | 10000011.11110111.00001000.00101101 | 10000011.11110111.00011011.11100111
Subnet mask | 11111111.11111111.11111000.00000000 | 11111111.11111111.11111000.00000000
Masked IP address | 10000011.11110111.00001000.00000000 | 10000011.11110111.00011000.00000000
Matching college | 131.247.8.0 = College 1 | 131.247.24.0 = College 3

## Slide 21: Determining subnet ID - example

## Slide 22: Use of subnet mask by hosts
So, the subnet mask helps routers
Subnet mask helps determine whether the destination host is on same subnet
Example of sending packets to two destinations

## Slide 23: Use of subnet mask by hosts
IP addresses
  Source : 192.168.1.3
  Home router : 192.168.1.1
  Destination 1: 192.168.1.153 (same subnet)
  Destination 2: 131.247.100.1 (different subnet)

## Slide 24: Use of subnet mask by hosts
ARP requests
  Destination 1: 192.168.1.153 (same subnet)
  Destination 2: 131.247.100.1 (different subnet)
      Destination MAC address = home router address

## Slide 25: Subnetting computations
Say you need about 500 computers/ subnet
  Need
    512
If the organization has a /15 network
3 part structure of 32-bit IP address looks as follows:

## Slide 26: Subnetting computations
Subnet ID has 32 – 15 – 9 = 8 bits
Subnet mask has 15 + 8 = 23 1’s
  Remaining bits are 0
Hence subnet mask is
  11111111.11111111.11111110.00000000
  255.255.254.0

## Slide 27: Subnet mask length and subnet size
The longer a subnet mask, the more the number of subnets
  But fewer hosts (computers)/ subnet
  Also, 3 IP addresses are lost for every subnet
Example
  Your organization has a Class B address, 131.247.0.0. Your largest department (network) has about 512 computers. What subnet mask should you use, assuming equal subnet sizes?

## Slide 28: Subnetting in IPv6
RFC 3587
  Standard lengths for network and subnet parts of unicast IPv6 addresses
    Global routing prefix (network part)
    Subnet ID
    Interface ID (host part)
  Simplifies routing

## Slide 29: Summary
Subnetting helps delegate IP addresses within large organizations
Subnetting can limit routing traffic
Subnetting is implemented using subnet masks
The 1’s in subnet masks indicate network ID and subnet ID
0’s indicate the host part

## Slide 30: Case study – An ISP in Texas

## Slide 31: Case study – An ISP in Texas
Subnet ID bits | Subnet | Aggregate | City
000 | 66.118.0.0 /21 |  | San Antonio
001 | 66.118.8.0 /21 |  | Austin
010 | 66.118.16.0/21 |  | Dallas
011 | 66.118.24.0/21 |  | Houston
100 | 66.118.32.0/21 | 66.118.32.0/20 | Houston
101 | 66.118.40.0/21 |  | Houston
110 | 66.118.48.0/21 | 66.118.48.0/20 | Houston
111 | 66.118.56.0/21 |  | Houston

## Slide 32: Hands-on exercise
Ipconfig /all to obtain subnet mask
Subnet mask in binary notation
Masked IP address of host
Number of hosts on subnet

## Slide 33: IT infrastructure design exercise
Subnets for each location