## Slide 1: Chapter 15
Wireless networks
ISM frequencies, LANs, PANs, MANs

## Slide 2: Contents
Business role of wireless LANS (WLANs)
ISM frequency bands
802.11a/b/g/n – WLANs/ Wi-Fi
802.15 – Bluetooth Personal area networks
802.16 – WiMax

## Slide 3: Business role of wireless networks
Quick and easy networking
In conjunction with laptops, networking everywhere
Pilot programs on city-wide LANs
Historical buildings

## Slide 4: Concerns with wireless
Primary concern is security
  Unauthorized access difficult to detect
Health
Speed and reliability

## Slide 5: ISM frequency bands
Wireless LANs are possible because of a very special category of wireless frequencies
Normally, licenses needed for wireless transmission
ISM bands are available for free, unlicensed use

## Slide 6: ISM frequency bands
Most of the popular ISM bands are not commercially useful
  Energy absorption by water vapor, foliage
    Microwave ovens operate at 2.45 GHz
In the U.S., ISM bands are defined in part number 18, title 47 of the FCC rules
  Code of federal regulations

## Slide 7: ISM frequency bands
ISM frequency | Band (tolerance)
6.78 MHz | ±15.0 KHz
13.56 MHz | ±7.0 KHz
27.12 MHz | ±163.0 KHz
40.68 MHz | ±20.0 KHz
915 MHz | ±13.0 MHz
2.45 GHz | ±50.0 MHz
5.8 GHz | ±75.0 MHz
6.525 GHz | ±600 MHz
24.125 GHz | ±125.0 MHz
61.25 GHz | ±250.0 MHz
122.5 GHz | ±500.0 MHz
245 GHz | ±1.0 GHz
RC remotes
WLANs
Use with 5G

## Slide 8: Wireless network categories
Three categories
  Local area networks
  Personal area networks
  Metropolitan area networks

## Slide 9: wireless vs wired LANs
No defined boundaries in wireless LANs
Very unreliable medium
Unprotected from co-existing signals on the medium
All stations cannot hear each other

## Slide 10: Wireless LAN architecture
Wireless LANs appear to higher layers (IP) as wired LANs
Large WLANs are built from small blocks

## Slide 11: Wireless LAN architecture

## Slide 12: Basic service set (BSS)
When a wireless station moves from one BSS to another, upper layers are not aware of the change
BSSs may overlap for redundancy
BSSs may be physically separated to obtain coverage in selected areas

## Slide 13: Access point (AP)
An access point (AP) acts like a station on the BSS and enables access to the DS to associated wireless stations
Stations (e.g. laptops) need to become associated with an access point (AP)

## Slide 14: Distribution system (DS)
The DS directs traffic between multiple BSSs
802.11 does not specify how DS should distribute messages between APs
A DS can combine multiple BSSs to create a wireless network of arbitrary size

## Slide 15: Portal
Data enters and leaves ESS at a portal
When DS determines that destination is not in the ESS, it directs traffic to the portal
All required frame format changes occur at the portal

## Slide 16: Security
Unlike wired LANs, any receiver near the BSS can listen to traffic
802.11 defines three cryptographic techniques to protect data
Default encryption mode is unencrypted

## Slide 17: MAC frame format

## Slide 18: 802.11 Physical layer
MAC layer in wireless LANs is designed to be independent of physical layer technology used
Unlike other technologies, wireless LAN physical layer adds header to account for unreliable transmission

## Slide 19: Physical layer format

## Slide 20: Popular 802.11 technologies
802.11 b/g (ch 14,15,18/ 19 in 802.11 standard)
802.11 a (ch 17 in 802.11 standard)

## Slide 21: 802.11n
Provided upto 600 Mbps data rate
Primary innovation was MIMO (multiple input multiple output)

## Slide 22: 802.11n evolution
Great reference for standards development process
  http://grouper.ieee.org/groups/802/11/Reports/tgn_update.htm
  4 candidate technologies voted in Nov ’04
  TGn obtained required majority in Mar ’07
  Technical and editorial issues in the standard resolved

## Slide 23: 802.11ac
Aimed to improve upon 802.11n
  Support multiple communication streams
  3 improvements over 802.11n
  Benefits require clear proximate access to AP

## Slide 24: 802.15 - Personal area networks
Bluetooth
  Communication over short distances (< 10m)
  Private, intimate group of participant devices
  Focus on small, power-efficient, inexpensive solutions

## Slide 25: Bluetooth vs. WLAN
Not intended for dedicated computing devices
Little or no direct connectivity to the world outside the link
No infrastructure necessary (e.g. AP, DS)
Focus on long battery life and low cost

## Slide 26: Bluetooth architecture
2.4 GHz band
Data rate of 1 Mbps
Frequency hopping spread spectrum (FHSS) modulation
Network unit is piconet

## Slide 27: Piconet architecture
A number of independent piconets may exist in one location
A device may be a slave on multiple piconets
  Called
But master on only one piconet at a time
Participation in a scatternet does not imply the ability to route between piconets

## Slide 28: Piconet architecture
Each piconet has a different physical channel
Physical channel defined by

## Slide 29: Bluetooth frame structure

## Slide 30: Device discovery
Special physical channel for inquiry requests and responses
Devices looking for nearby devices are called inquiring devices
Devices willing to be found are called discoverable devices

## Slide 31: Device connection
Once a pair of devices discover each other, connection procedure begins
One device must be connectable
Other device must page on connection channel of connectable device

## Slide 32: WLAN and WPAN co-existence
802.11b/g and 802.15 operate at 2.45GHz
Bluetooth signals interfere with WLAN
IEEE 802.15.2
  Two kinds of co-existence mechanisms to minimize interference

## Slide 33: WLAN and WPAN co-existence
Collaborative
  MAC layer
  Physical layer
Non-collaborative

## Slide 34: Bluetooth categories
Normal data rate
High data rate
Low data rate

## Slide 35: Summary
Why wireless networks are useful
Why different categories of wireless networks
ISM frequency bands
Comparisons between WLAN, WPAN and WMAN

## Slide 36: Case study – Oil industry
Vertically integrated
Monitoring fuel levels in gas stations
Improved monitoring of pipelines
Improved monitoring of remote oil pumps

## Slide 37: Hands-on exercise
AirPCap and Wireshark

## Slide 38: IT infrastructure design exercise
LAN network in Amsterdam
  Technology choice