## Slide 1: Chapter 1
Introduction

## Slide 2: Contents
Definition
Utility of computer networking
Technology milestones
Packetization
Layering
TCP/ IP model
OSI model
Principles of Internet protocols

## Slide 3: Definition
Business Data Communications
Used synonymously with “computer networking”

## Slide 4: Typical data network

## Slide 5: Unique features of computer networks
Common set of technologies support all networked computer applications
Basic principles unchanged for over 4 decades
An essential component of modern economy

## Slide 6: Utility of computer networking
One of the world’s largest industries
Networking infrastructure is a driver of the economy
Digital economy likely to exceed $4Trillion by 2016

## Slide 7: CISCO Global IP traffic forecast
 | 2014 | 2019 | CAGR 2014-2019
By type (peta bytes/ month) |  |  | 
Fixed Internet | 39,909 | 111,899 | 23%
Mobile data | 2,514 | 24,221 | 57%
By segment |  |  | 
Consumer | 47,740 | 138,415 | 24%
Business | 12,108 | 29,563 | 20%
By geography |  |  | 
Asia-Pacific | 20,729 | 54,434 | 21%
North America | 19,628 | 49,720 | 20%
Western Europe | 9,601 | 24,680 | 21%

## Slide 8: What’s in it for me?
Bureau of Labor Statistics estimates (2012)
  Network and computer system administrators
    2012 employment : 366,400
    Median pay : $72,560
Growth rate: 12% (until 2022)

## Slide 9: Technology milestones
Telegraph
  Information carried as electrical signals over wires
Multiplexing
Circuit switching
  March 10, 1891, Strowger switch patented
    Tampa connection - Buried in St. Pete - http://en.wikipedia.org/wiki/Almon_Strowger
Packet switching
  Signals sent and switching performed only when information ready to be transferred

## Slide 10: Telegraph

## Slide 11: Multiplexing and switching
Multiplexing
Circuit switching

## Slide 12: Packet switching
Packet switching (1969 - )

## Slide 13: Data communications timeline

## Slide 14: Circuit switching vs packet switching
A circuit is an electronic closed-loop path among two or more points
Packet switches are called routers
Circuit switched networks typically bill by the minute
Packet switched networks typically bill by the MB

## Slide 15: Packetization overview
Packetization is
Each segment or packet has two parts

## Slide 16: Packets analogy

## Slide 17: Packetization in retail

## Slide 18: Factors favoring packet switching over circuit switching
Increase in interactive data traffic (as opposed to voice traffic) has increased “burstiness” of data (high ratio of peak usage to mean usage)
Packet switching enables efficient utilization of communication links by averaging needs among large numbers of users

## Slide 19: Traffic aggregation

## Slide 20: Advantages of packetization
Communication link costs are now very high relative to switching costs
Eliminates single points of failure in data communication systems
Ease of transport

## Slide 21: Layering
Arranging functionality in a hierarchical manner, such that
This is how we create and process packets
Example (corporate)

## Slide 22: Layering examples
Example (software)

## Slide 23: Advantages of layering
Specializes technology development
Separation of functionality
Simplification in adding new technology

## Slide 24: Layering in data communication

## Slide 25: Typical packet structure
Five important datacomm tasks
  User needs (e.g. get web page, web page body)
  Segmentation and reassembly
  Identifying and locating destination
  Error control
  Signaling - Converting data into a form suitable for transmission over wires

## Slide 26: Typical packet structure
These and other related datacomm tasks are accomplished by adding additional required information to information packets
Routers perform packet switching

## Slide 27: Important header information
Networking task | Header information
Specify user needs | User commands
Segmentation and reassembly of packets | Sequence numbers
Identifying and locating destination | Address
Error control | Error check
Signaling | None

## Slide 28: Typical packet structure
A typical packet contains
  Information sent from the layers above
  and

## Slide 29: 5-layered TCP/ IP stack
Modern computer networks implement layering in 5 layers
Called the TCP/ IP stack
Integrates two popular sets of technologies

## Slide 30: Layer names and tasks
Layer number | Layer name | Networking task | Header information
5 | Application | Specify user needs | User commands
4 | Transport | Segmentation and reassembly of packets | Sequence numbers
3 | Network | Identifying and locating destination | Address
2 | Data-link | Error control | Error check
1 | Physical | Signaling | None

## Slide 31: TCP/ IP stack layer technologies

## Slide 32: OSI model
OSI – Open Systems Interconnection
Early networks involved multiple networking technologies
Even the current dominant TCP/ IP 5-layer stack integrates two major technologies – TCP/ IP and Ethernet

## Slide 33: OSI model
The OSI model is a logical structure for communications networks, standardized by the International Organization for Standardization (ISO)
Current status: Useful as an introduction to data networks

## Slide 34: OSI model

## Slide 35: OSI model strengths and weaknesses
Strengths
Weaknesses

## Slide 36: OSI and TCP/ IP

## Slide 37: Principles of Internet protocols
The Internet would be a network of multiple independent networks
Multiple applications could use the Internet, including those not yet conceived

## Slide 38: Principles of Internet protocols
Standardized message block to serve any application
-- Baran 1964

## Slide 39: TCP/ IP technologies by layer

## Slide 40: A typical computer network

## Slide 41: Standards reference
Internet technology standards are publicly available as Requests For Comment (RFCs)
  http://www.ietf.org/rfc.html
Highly recommended standards
  Email: http://www.ietf.org/rfc/rfc0821.txt
  HTTP: http://www.ietf.org/rfc/rfc2616.txt
  TCP: http://www.ietf.org/rfc/rfc0793.txt
  IP: http://www.ietf.org/rfc/rfc0791.txt
  TCP/ IP tutorial: http://www.ietf.org/rfc/rfc1180.txt
  Domain names: http://www.ietf.org/rfc/rfc1034.txt

## Slide 42: Rest of the course
Chapters 2 – 6: Layers of TCP/ IP stack
Chapters 7 – 11: Technologies supporting networking
Chapters 12 – 13: Technologies related to computing
Chapter 14: Managerial issues in IT infrastructures
See anatomy of a web request

## Slide 44: Case study – Domino’s Pizza
Pizza tracker
Bringing the computer network into the food industry
Anecdotal evidence is positive
Almost 40% of orders come online

## Slide 45: Hands-on exercise
Traceroute

## Slide 46: IT infrastructure design exercise

## Slide 47: Summary
Why computer networks
Important milestones in datacomm
Why packetization
Typical packet structure
Why layering
Layers of TCP/ IP
Functions of each layer in TCP/ IP model
OSI model
Internet protocol principles