## Slide 1: Chapter 2
Physical Layer

## Slide 2: Contents
Functions of the Physical Layer
Physical media and their properties
Signals and their properties
Importance of binary signals
Signal representation of data
Multiplexing

## Slide 3: Physical layer service definition
Provide transparent transmission of a bit stream over a circuit built from some physical communications medium
ATIS Telecom glossary
  http://www.atis.org/glossary/default.aspx

## Slide 4: The need for signals
Data cannot be transmitted
But data can be converted to signals
Signal are detectable transmitted energy that can be used to carry information
E.g. How are you reading this slide

## Slide 5: Data to signal

## Slide 6: Special feature of the Physical Layer
Physical layer interacts with nature
Signal transmitting properties of chosen media are important

## Slide 7: Physical media and their properties
The physical medium is the transmission path along which a signal propagates
Media are chosen for their special properties that enable efficient transmission (movement) of signals

## Slide 8: Copper wire as physical medium
Copper is a very good conductor of electricity and is relatively abundantly available
When used as a physical medium in computer networking, 8 individual strands of copper wire are organized as four pairs

## Slide 9: Categories of UTP cables
Categories range from Cat-1 to Cat-6
  http://en.wikipedia.org/wiki/Category_5_cable
Cable type | Max data rate
Cat 3 | 10 Mbps
Cat 5e | 1,000 Mbps = 1Gbps
Cat 6 | 10 Gbps

## Slide 10: Categories of UTP cables
Cat 3 cable
Cat 5 cable

## Slide 11: Cable connectors
Cat5e cables end in RJ 45 connectors
Conductor identification | Color code | Use
Pair 1 | White-Blue/ Blue | -
Pair 2 | White-Orange/ Orange | Transmit data
Pair 3 | White-Green/ Green | Receive data
Pair 4 | White-Brown/ Brown | -

## Slide 12: Optical fiber as physical medium
Optical fiber is a thin strand of glass that guides light along its length
Typically aggregate traffic is carried over fiber

## Slide 13: Aggregating network traffic from copper to fiber

## Slide 14: Submarine optical fiber installation

## Slide 15: Optical fiber as Physical medium
Glass is a good conductor of light
Works on the principle of Total Internal Reflection

## Slide 16: Types of optical fiber
Multiple mode
Single mode

## Slide 17: Construction of optical fiber

## Slide 18: Data vs. Signals
Data:
Signal:

## Slide 19: Signals and their properties
Signals are changes in energy that can be detected at the receiver
Good signals can provide
  Multiplexing

## Slide 20: Impacts of improved signaling
Easy reception
Noise resistance

## Slide 21: Impacts of improved signaling
Efficient utilization of bandwidth
Multiplexing

## Slide 22: Categories of signals
All signals involve creating change at the sending end that can be detected at the receiving end
  e.g:
In data communication, we find it easiest to do one of the following:

## Slide 23: Categories of signals
Chart: 
Chart: 
Digital signal – signals in which information is represented in discrete steps
Analog signal – signals that have a continuous nature, and not discrete or pulsed

## Slide 24: Analog signals
Are actually surprisingly easy to generate in nature
  E.g. height of any point on a spinning wheel

## Slide 25: Commonly used signals
AM (amplitude modulation)
PM (phase modulation)
QAM (quadrature amplitude modulation)
Manchester encoding

## Slide 26: Commonly used signals

## Slide 27: Noise and binary signals
Noise is any disturbance that interferes with the normal operation of a device
Signal detection over long distances over any medium is constrained by noise

## Slide 28: Noise and binary signals
There are many sources of noise
  External interference, heating, cross-talk etc.
Good signals and good media work together to help detect signals and reduce noise

## Slide 29: Impact of noise on signals
Chart: Transmitted signal
Chart: Received signal

## Slide 30: Need for binary signals
Computer systems use binary representation for all data
Consider AM (easy to understand)
Chart: 3-level signal transmitted
Chart: 2-level signal transmitted

## Slide 31: Binary signals
Detection rule for 2 level signal (binary)
  If amplitude < first gridline,
  data = 0
  else data = 1
Detection rule for 3 level signal (ternary)
  If amplitude < first gridline,
  data = 0
  else if amplitude between 2 gridlines
  data = 1
  else data = 2
Clearly ternary systems are more prone to errors
Chart: 2-level signal + noise
Chart: 3-level signal + noise

## Slide 32: Shannon’s theorem
How much data can you send over a medium?
  Defined by the Shannon-Hartley theorem
    C is the channel capacity in bits/ second
    B is the channel bandwidth in Hertz
    S and N are the signal and noise levels in Watts
      S/N ratio commonly known as

## Slide 33: Hertz
Unit of frequency
  One cycle per second
Phone line
  Sends signals in frequency range 0Hz – 3,400 Hz
  Bandwidth = 3,400 – 0 = 3,400 Hz

## Slide 34: Signaling
Sending data as signals
Consider sending the word “Hello”
How to send letters h, e, l, l, o on the wire
  Sender side
    Step 1:
    Step 2:
  Receiver side
    Step 3:
    Step 4:

## Slide 35: ASCII code for binary representation of data
Standard method to convert characters to binary is ASCII code
  Numbers 0-127 represent common characters
  http://www.asciitable.com
  Decimal to binary conversion shown later (with IP addresses), just accept for now
Letter | Decimal | Binary
h | 104 | 01101000
e | 101 | 01100101
l | 108 | 01101100
o | 111 | 01101111

## Slide 36: Unicode
Used to represent characters in almost all languages
  Including over 75,000 Chinese characters
ASCII code = Unicode for English characters
Other characters
  945 – 969 for the Greek characters α – ω
  Try typing 03c9 Alt+x in Word

## Slide 37: Amplitude modulation signaling
Chart: 

## Slide 38: Amplitude modulation signaling
Chart: 

## Slide 39: Receiver operation
The receiver keeps track of bit periods
  If a wave is received during the bit period, it is interpreted as 1, otherwise 0
These bits are decoded as letters
  And the sender’s message is received

## Slide 40: Multiplexing
Sending multiple signals simultaneously on the same medium, e.g.
Extremely important milestone in data communication

## Slide 41: Networking without multiplexing
NYC around 1900

## Slide 42: Why multiplexing
Previous pictures show NYC before multiplexing was possible
  Multiple telephone lines between same locations required multiple physical cables
    Result:
With multiplexing, most cables on one tower can be replaced with one cable

## Slide 43: Multiplexing categories
Send signals at different frequencies
  Called frequency division multiplexing (FDM)
Or, send signals at different times
  Called time division multiplexing (TDM)
Fortunately, multiplexing can be easy to do
  Following example shows frequency division multiplexing with AM

## Slide 44: AM multiplexing example - overview
2 signals (simple sine waves in example)
2 carriers (one for each signal)
  Think of 2 radio stations
Each station modulates its carrier with its signal (step 2 in our previous example)

## Slide 45: AM multiplexing example - overview
Receivers receive this aggregate
Receivers demodulate to recover signal
  step 3 in our previous example
See file AM_multiplexing_example.xlsx on companion website

## Slide 46: AM example - signals
Chart: 
Chart: 

## Slide 47: AM example - carriers
Chart: 
Chart: 

## Slide 48: AM example – modulated carrier 1
Chart: 

## Slide 49: AM example – modulated carrier 2
Chart: 

## Slide 50: AM example – signal in medium (sum of 2 modulated carriers)
Chart: 

## Slide 51: Demodulation in AM example
This is the process of recovering the signal of interest at the receiver
Fairly simple to do
  Multiply signal in medium by a signal at same frequency as carrier
  This removes all other signals
  Remove noise by “averaging”

## Slide 52: AM example – demodulated signal 1
Chart: 

## Slide 53: AM example – demodulated signal 2
Chart: 

## Slide 54: AM example–recovered signal 1
Chart: 

## Slide 55: AM example-recovered signal 2
Chart: 

## Slide 56: Summary
Signaling at physical layer
Properties of nature enable signaling
Good signals enable reliable detection in the presence of noise and other signals
UTP – Cat3 (slow) and Cat5e (faster)
Optical fiber - Multi-mode (short-range) and single-mode (long-range)
Multiplexing enables efficient utilization of media

## Slide 57: Case study – Smart grids
The power grid is considered the greatest achievement of humanity in the 20th century
To lower power costs, we need to smoothen power demand

## Slide 58: Case study – Smart grids
Power generation prices vary during the day, depending upon power source
Market-oriented mechanism would reduce consumption during high price periods
Power lines can be used to transmit pricing information
Home owners may even store power when cheap and sell power when expensive

## Slide 59: Hands-on exercise
Calculating bit period
Modifying data for new bit period
Modifying carrier frequency
Plotting graphs
Calculating amplitude of modulated signal
Interpreting modulated carrier

## Slide 60: IT infrastructure design exercise
Choice of medium for each location
Estimating wire length
Choice of medium for connecting locations