## Slide 1: Chapter 7
Support infrastructure for networking
DHCP, NAPT, ARP, DNS

## Slide 2: Contents
DHCP (Dynamic host configuration protocol)
RFC 1918 non-routable addresses
Network address translation
Address resolution protocol
Domain Name System
Home networking

## Slide 3: DHCP
A big part of the usefulness of IP addresses is the flexibility in their assignment
However, manual assignment is very prone to errors

## Slide 4: IP address allocation efficiency
With 32-bit addresses, there can be 232 = 4 billion addresses
However, these addresses are not assigned very efficiently
Further, at any given time, only a small fraction of the computers are actually communicating with other computers outside the organization

## Slide 5: Solving IP address availability
So, the real fear is that we could be running out of IP addresses
The long-term solution is to increase the pool of IP addresses
Dynamic host control protocol (DHCP) is one part in a 3-part short-term solution

## Slide 6: The DHCP solution
DHCP enables programmatic assignment and collection of IP addresses
Defined in RFC 2131 (March 1997)
Addresses may be allocated in 3 ways:

## Slide 7: DHCP dynamic allocation
Allows automatic reuse of an address when it is no longer needed by the computer to which it was assigned
Each subnet has access to at least one DHCP server
All DHCP clients look for a DHCP server upon startup to get network parameters

## Slide 8: DHCP server and client settings

## Slide 9: DHCP operation timeline

## Slide 10: DHCP dynamic allocation
The DHCP server provides an IP address for a fixed duration in response to a client’s DHCP request
The DHCP server also provides all network configuration information the client needs to operate

## Slide 11: DHCP – address leasing
Duration of address assignment is called lease-time
The client can request the DHCP server for an extension of the lease before the lease expires
In a typical DHCP client-server interaction

## Slide 12: Sample dhcpd.conf
Dynamic allocation range
Manual allocation
Network options
option domain-name “datacomm.example.com";
option domain-name-servers 10.1.1.1, 10.2.1.1, 10.3.1.1;
option routers 10.1.1.254;
option subnet-mask 255.255.255.128;
default-lease-time 21600;
subnet 10.1.1.128 netmask 255.255.255.128 {
range 10.1.1.236 10.1.1.253;
}
host www {
hardware ethernet 00:06:5B:CE:39:05;
fixed-address 10.1.1.2;
host-name “www.datacomm.example.com";
}

## Slide 13: Non-routable Addresses
Address reuse
Certain IP addresses have been defined to be reusable as many times as necessary
Defined in RFC 1918 (1996)

## Slide 14: Non-routable address blocks
One class of special IP addresses
  Recall from Network layer chapter
Three blocks have been defined in RFC 1918
May be used internally without any co-ordination with any Internet registry
Routers do not advertise routes with non-routable addresses to other organizations

## Slide 15: Using non-routable addresses

## Slide 16: Network Address Translation (NAT)
Third component of 3-part solution to IP address shortage
Definition (RFC 2663)

## Slide 17: NAT
NAT is specified in RFC 3022
Until IPv6 is universally deployed, NAT and RFC 1918 expands the availability of IP addresses
Many experts hate NAT because it does not preserve IP addresses end-to-end

## Slide 18: Basic NAT operation

## Slide 19: NAT in use
The single external IP address can support many clients in the internal network
The NAT router translates between internal IP addresses and its own external address
Designed to support outbound connections from the internal network

## Slide 20: Using NAPT and RFC 1918 addresses

## Slide 21: Network Address Port Translation
Abbreviated as NAPT
Described in RFC 3022
NAPT can vastly expand the availability of IP addresses by enabling each IP address to serve up to 65,536 separate connections to each remote host

## Slide 22: Address Resolution Protocol (ARP)
ARP is used to find Ethernet addresses at the data-link layer for destinations with a known IP address
Defined in RFC 826 (1982)
Global routes are composed of a sequence of next hops

## Slide 23: Need for ARP
But to physically send the packet to the next hop, we need to know its Ethernet (MAC) address
ARP is used to discover the MAC address of the device at the next hop when its IP address is known
ARP links addressing at 2 layers – network and data link

## Slide 24: ARP operation

## Slide 25: ARP operation
Before the first packet in a stream is transmitted, the sender creates a special packet called an ARP request and broadcasts it on the LAN
The computer/ router with the address replies with its MAC address

## Slide 26: ARP packets
ARP request
  Sender MAC Address : 00:11:50:3a:da:22
  Sender IP address : 192.168.2.11
  Target MAC Address : 00:00:00:00:00:00
  Target IP address : 192.168.2.1
ARP response
  Sender MAC Address : 00:18:8b:c9:24:6b
  Sender IP address : 192.168.2.1
  Target MAC Address : 00:11:50:3a:da:22
  Target IP address : 192.168.2.11
Place-holder address
Response from target

## Slide 27: ARP data
Resolved MAC addresses are saved in cache for some time
  Can be retrieved using arp -a

## Slide 28: Domain name system (DNS)
Computers are uniquely identified on the Internet by their IP addresses
However, IP addresses are not very easy to remember
The domain name system was developed to make it easier for humans to identify computers

## Slide 29: DNS use

## Slide 30: The need for a Name Service
Initially, the Internet was small, and all users maintained a hosts file to translate names to IP addresses
The need was recognized for a system

## Slide 31: DNS
The solution was domains and DNS
  RFC 1034
  RFC 1035
Domain names are arranged hierarchically, originating from a common root
  Hierarchy based on administrative structure, e.g.
As we move from right to left, domain names identify increasingly specific units of the network

## Slide 32: Domain naming hierarchy

## Slide 33: Domain hierarchy
The name at each hierarchical level is a domain
  Domains are sub-domains of their parent domains
  The domain’s name includes all names to its right
  Each domain maintains jurisdiction over its immediate sub-domains, and only these sub-domains
  Each domain is responsible to translating these sub-domain names to IP addresses

## Slide 34: Domain names
The rightmost part of all domain names is . which represents the entire Internet
All domain names are unique
The hierarchical structure of the Internet enables delegation of naming services

## Slide 35: Top level domains
A number of top-level domains have been created
  Root zone database at www.iana.org
  Open domains
  Limited domains
  Industry-specific domains
  Country domains

## Slide 36: DNS lookups
Every computer on the Internet knows the IP address of a name server it can use
When a user types a URL, the resolver in the computer first asks its name server for the IP address corresponding to this URL

## Slide 37: Typical DNS Query
# dig www.buffalo.edu @ mother.usf.edu
;; Got answer:
;; QUESTION SECTION:
;www.buffalo.edu. IN A
;; ANSWER SECTION:
www.buffalo.edu. 86400 IN A 128.205.4.175
;; AUTHORITY SECTION:
buffalo.edu. 71951 IN NS ns.buffalo.edu.
buffalo.edu. 71951 IN NS sybil.cs.buffalo.edu.
Buffalo.edu. 71951 IN NS accuvax.northwestern.edu.
;; ADDITIONAL SECTION:
ns.buffalo.edu. 71951 IN A 128.205.1.2
sybil.cs.buffalo.edu. 53404 IN A 128.205.32.8
accuvax.northwestern.edu. 11624 IN A 129.105.49.1
;; Query time: 3 msec
;; SERVER: 131.247.100.1#53(mother.usf.edu)
Query
Name server
IP address
Name servers
Security measure
NS IP address
Success

## Slide 38: DNS Operation
Domains are called zones in the context of the domain name service
Name servers have two kinds of data
If the name for a foreign zone is requested, a recursive query results if there is no entry in cache

## Slide 39: Recursive DNS query resolution

## Slide 40: DNS query resolution
pns:~# dig +trace www.usf.edu
; <<>> DiG 9.2.4 <<>> +trace www.usf.edu
. 77639 IN NS E.ROOT-SERVERS.NET.
(and other root name servers)
edu. 172800 IN NS E.GTLD-SERVERS.NET.
(and other .edu name servers)
usf.edu. 172800 IN NS justincase.usf.edu.
usf.edu. 172800 IN NS mother.usf.edu.
(and other usf.edu name servers)
www.usf.edu. 600 IN A 131.247.80.88

## Slide 41: IP address volatility and the benefit of DNS

## Slide 42: DNS Configuration
Time to live
NS start of authority
Admin email: hostmaster@example.com
Name server update counter
Resource records
www.example.com is at
192.168.16.129
Delegation: NS for test.example.com is at
demo.example.com (192.168.16.143)
$TTL 86400
@ IN SOA pns.example.com. hostmaster.example.com. (
serial 2008072701
)
IN NS pns.example.com.
IN MX 10 mail.example.com.
pns A 192.168.16.129
www A 192.168.16.129
mail A 192.168.16.130
test NS demo
demo A 192.168.16.143

## Slide 43: DNS Configuration
The administrator for the .com. domain delegates authority for example.com
The example.com name server authoritatively defines the IP addresses for all resources in its domain
example.com delegates responsibility for test.example.com to demo.example.com

## Slide 44: DNS Configuration
TTL
  Zones will not change for the next 86400 seconds (1 day)
Serial

## Slide 45: Putting it all together: Home networking
We have now seen all components of a typical home network
The wireless router acts as a NAPT router and DHCP, DNS server

## Slide 46: Home networking
(1) ipconfig output on home computer
(2) Wireless router status page
Wireless router provides network services on internal address
WAN address visible to outside world
(3) External IP address

## Slide 47: Home networking
WAN IP address can be looked up at ARIN website
  Will show the ISP’s address pool

## Slide 48: Summary
Why DHCP
Why non-routable IP addresses
Why ARP
Why DNS
Components of home network

## Slide 49: Case study – Web hosting
DNS and virtual hosting enable ISP services
For example, consider Aabaco small business
nslookup www.green-tooth.com
  Non-authoritative answer:
  www.green-tooth.com canonical name = stores.yahoo.net.
  stores.yahoo.net Address: 68.142.205.137
  www.invitationshack.com canonical name = stores.yahoo.net.
  stores.yahoo.net Address: 68.142.205.137

## Slide 50: Case study – Web hosting

## Slide 51: Hands-on exercise
nslookup

## Slide 52: IT infrastructure design exercise
Services requiring externally addressable IP addresses
Add Internet connection
Include NAPT device