## Slide 1: Chapter 10
Wide Area Networks

## Slide 2: Contents
The need for Wide area networks (WANs)
Point-to-point approaches
Statistical multiplexing, TDM, FDM approaches
Dial-up, T/ DS links
X.25, Frame relay, ATM
SONET
DWDM
WANs and TCP/ IP stack

## Slide 3: Definition
WANs are physical or logical networks that provide data communications to a large number of independent users. These users are usually spread over a larger geographic area than a LAN

## Slide 4: The need for WANs
LANs are very effective at connecting computers within offices
Links are short, so dedicated link to each PC is not too expensive
But many organizations have offices in many states and countries
Web pages, email servers are located world-wide
As users spread over large distances, link costs become very high

## Slide 5: The need for WANs (contd.)
Broadcast lowers costs of LAN equipment
But as number of users increases, CSMA slows down the network significantly
As number of network users increases, need mechanisms to merge traffic from multiple users

## Slide 6: Roads and computer networks
There are many similarities between the challenges and design solutions used in road networks and computer networks
Neighborhood networks are like LANs
Interstate networks are like WANs

## Slide 7: Local intersection as LAN node
Stop sign promotes carrier sensing
White car will wait till black car passes

## Slide 8: Interstate exit as WAN node
Merging lane: Entry ramp for local traffic
Existing traffic does not stop for merging traffic
Shared lanes
Merging lane: Exit ramp for local traffic

## Slide 9: Categories of WANs
Point-to-point
Statistical multiplexing
TDM
FDM/ WDM
MPLS

## Slide 10: Point-to-point WANs
Earliest WANs used dial-up networking
Phone lines
Internet in 1969

## Slide 11: T/ DS carriers
Phone companies realized business opportunity in providing data services
Combined (multiplexed) data carrying capacity of multiple phone lines to provide high speeds
Offered as T/ DS carriers

## Slide 12: WAN built using T-carriers

## Slide 13: T/ DS carriers
Formally, t-carriers are the physical line, DS is the signal carried by the line
Offer point-to-point connection like dial-up
No. of phone lines aggregated | T-carrier name | DS name | Data rate
1 |  | DS-0 | 64 kbps
24 | T-1 | DS-1 | 1.544 mbps
96 | T-2 | DS-2 | 6.312 mbps
672 | T-3 | DS-3 | 44.736 mbps

## Slide 14: Statistically multiplexed WANs
Point-to-point is very inefficient when network grows
Statistical multiplexing allows WANs to aggregate traffic

## Slide 15: Reducing “burstiness”
Chart: Time of day
| 0.33333333333333331 | 0.37500000000000017 | 0.41666666666666724 | 0.45833333333333293 | 0.5 | 0.54166666666666596 | 0.58333333333333304 | 0.62500000000000033 | 0.6666666666666663 | 0.70833333333333304
A | 80 | 85 | 75 | 80 | 35 | 25 | 15 | 15 | 15 | 15
B | 15 | 15 | 15 | 15 | 35 | 40 | 55 | 65 | 85 | 75
A+B | 95 | 100 | 90 | 95 | 70 | 65 | 70 | 80 | 100 | 90

## Slide 16: Virtual circuits
Connection | Virtual-circuit ID
A-A | 1
B-B1 | 2
B-B2 | 3

## Slide 17: X.25/ Frame relay/ ATM
Shared network services offered by telcos
End users connect to shared network using point-to-point links such as T1/ T3

## Slide 18: X.25/ Frame relay/ ATM
When data packets enter shared network, carrier assigns label based upon destination
Shared network uses labels to direct packets to correct destinations
Each label is called a virtual channel

## Slide 19: X.25/ Frame relay/ ATM
X.25
Frame relay
ATM

## Slide 20: TDM WANs
Available line data rate divided into time slots
Each virtual channel given one or more slots
Commercially available as SONET services
Pricing generally dependent on distance: ~ $15/ mbps/ mile

## Slide 21: TDM WANs
X.25/ Frame relay/ ATM often transported over SONET links
SONET data rates first standardized in 1988 by CCITT
SONET service names | Data rate | Data + overhead
OC-1 | 50.112 mbps | 51.84 mbps
OC-3 | 150.336 mbps | 155.52 mbps
OC-12 | 601.344 mbps | 622.08 mbps
OC-48 | 2.405,376 gbps | 2.488,320 gbps
OC-192 | 9.621,504 gbps | 9.953,280 gbps
OC-768 | 38.486,016 gbps | 39.813,120 gbps

## Slide 22: FDM WANs
Optical fiber has very high bandwidth
Available line bandwidth split into multiple lower bandwidth channels

## Slide 23: FDM WANs
DWDM channel frequencies standardized by ITU-T as ITU grid in 2001
DWDM commonly used in network core
Each FDM channel on a DWDM link may transport a SONET signal, which in turn may transport multiple ATM channels

## Slide 24: WANs and TCP/ IP stack
Where are WAN technologies positioned on the TCP/ IP stack?
Typically, multiple WANs traversed by packet from source to destination
Routers interface between WANs

## Slide 25: WANs and TCP/ IP stack
Traceroute to Google

## Slide 26: Summary
WANs are long distance links that aggregate traffic from multiple networks
WANs generally have very high data rates
WAN types include point-to-point, statistically multiplexed, TDM and FDM
Carriers define virtual circuits for each source-destination pair of nodes
WANs operate at the data link layer

## Slide 27: Case study – UAVs
Remote wars were fought with soldiers
Now, increasingly de[end upon satellite based WAN networks
UAVs

## Slide 28: Hands-on exercise
Web-page debugging
  Large web pages generate unnecessary WAN traffic
  Simple tools can help debug problems
    Browser → Right click → Inspect element → Network tab

## Slide 29: IT infrastructure design exercise
Choosing appropriate WAN technologies
Adding routers to the network