## Slide 1: Key Concepts in Chapter 4
Enterprise Network Infrastructure and Security © Prospect Press Thomas Case

## Slide 2: The OSI Model
Like enterprise networks, the Open Systems OSI model and its communication functions are part of EA’s technology architecture layer.
It has two major components: the reference model and protocols. The reference model describes the seven layers in the model. Protocols allow each layer of a network-attached device to communicate with the corresponding layer of another device. Senders add header fields at each layer tell receivers how data should be handled.

## Slide 3: The TCP/IP Model
The five-layer TCP/IP model provides a framework for understanding how data is transferred between different network locations and describes the protocols used to do so.
TCP/IP communication is called host-to-host communications; a host is a device that provides access to a network via a user interface, specialized software, a network address, and a protocol stack.
Like OSI model layers, each TCP/IP layer provides basic functions needed to transfer data, and logical connections between corresponding layers in communicating devices are used. The unit of information sent by the protocol at a particular TCP/IP (or OSI) layer is called a protocol data unit (PDU).

## Slide 4: TCP/IP Addresses and the Application Layer
The TCP/IP model uses three different types of addressing.
Port numbers are included in Transport layer headers to identify applications in communicating hosts; these numbers serve as application addresses.
IP addresses are included in Network layer header fields when packets are created, and physical MAC addresses are included in Data Link layer headers when frames are created.
TCP/IP’s Application layer supports standardized data exchange for client-server and other distributed applications.
Some Application layer protocols support common user activities such as web browsing, email, uploading and downloading. Others provide various support services, such as routing, domain name services, host configuration, and network management.

## Slide 5: Application Layer Technologies
Application layer technologies are deployed to enhance network performance, efficiency, and security.
There is a limited range of hardware-only technologies for the Application layer, but an extensive array of services are deployed as software or as combinations of hardware and software. Application layer hardware technologies include servers, load balancers, application layer switches, and application firewalls.
A load balancer receives client requests and distributes them to the servers in a cluster or server farm that available to fulfill them; basically, it acts as a traffic cop to ensure that no server is overworked.
An Application layer switch is a type of multilayer switch that uses Application layer information such as a URL, an HTTPS session ID or cookie to make switching decisions; like load balancers, they are typically deployed at server locations to expedite delivery of client requests.
An Application layer firewall implements rules to block or allow data/messages to and/or from an application. They do in-depth inspections of packet contents and strive to prevent malicious code from reaching or infecting the applications that they protect.

## Slide 6: Transport Layer Security (TLS) and the Transport Layer
Transport Layer Security (TLS) is a cryptographic (encryption) protocol that provides host-to-host communications security. HTTPS uses TLS by default.
Although it has “Transport Layer” in its name, TLS is located between the Application and Transport layers in the TCP/IP model. Because it runs on top of TCP and other Transport layer protocols, TLS essentially bridges the Application and Transport layers.
The Transport layer establishes, and monitors communication channels that applications use to exchange data. It uses port numbers to define how data should be delivered to applications on destination hosts.
The Transport layer provides two types of data delivery services: a connection-oriented service involves the creation and termination of host-to-host communication sessions and data exchanges; a connectionless service does not require a host-to-host communication session for data transfer.
TCP is a connection-oriented protocol. It is reliable; data sent using TCP is guaranteed to be delivered to the receiver. If data is lost or corrupted in transit, TCP ensures that it is resent.
UDP is a connectionless protocol that does not require establishing communication sessions or acknowledgment of transmitted datagrams; datagram is the term used to refer to the PDU created by UDP at the Transport layer.

## Slide 7: Transport Layer Technologies
There are several important Layer 4 technologies including Layer 4 switches/gateways, load balancers, and firewalls which are illustrated in Figure 4-14.
These technologies may be deployed solely as software but are most commonly a combination of hardware and software.
A Layer 4 switch is a multilayer switch that uses the port numbers in Transport layer headers for switching decisions and directing incoming traffic to specific applications, services, or servers.
A Layer 4 load balancer uses port numbers in Transport layer headers to distribute incoming client requests across available servers; like other load balancers, it strives to optimally distribute incoming requests to facilitate quick responses from servers.
Layer 4 firewalls filter traffic based on source and destination IP addresses, ports, and protocols; they also actively track communication sessions and allow/deny traffic based on the state of those sessions using a process called stateful packet inspection or dynamic packet filtering.

## Slide 8: TCP/IP’s Network Layer
The Network layer enables connections between independent networks and enables packets to be transferred them. Internetworking and logical addressing are some key communication functions that this layer performs.
Internetworking involves transferring data from one network to another. The network-to-network transfer process in called routing and is supported by host identification and host addressing. These enable data to be transferred from a host in one network to a host in another network via logical communication channels called virtual circuits.
Host addressing allocates logical Network layer addresses to hosts. These are needed to identify hosts and the networks and subnets in which they are located.
IP addresses are logical host addresses used in TCP/IP networks. A host needs an IP address to use the TCP/IP network to create, send, and receive Network layer PDUs (called packets). Source (sender) and destination (receiver) IP addresses are included in Network layer headers. Each packet is treated as a datagram that can be independently routed from sending to destination host.
Routing is performed by a router—a networking technology deployed as software or a hardware/software combination—that transfers packets between networks. When sender and receiver hosts are in different networks, packets are forwarded from a router in the sender’s network to an appropriate next-hop router for further relaying to the destination network. A router in the destination network delivers the packet to the destination host.

## Slide 9: Network Layer Protocols and Network Address Translation
Internet Protocol (IP) is the principal Network layer protocol. It defines two host addressing systems: IPv4 and IPv6. Internet Protocol version 4 (IPv4) uses 32-bit IP addresses; Internet Protocol version 6 (IPv6) uses 128-bit addresses.
IPsec (Internet Protocol Security) is a protocol suite that authenticates and encrypts packets in an IP network to provide secure host-to-host communication.
Other Network layer protocols are identified in Figure 4-15.
Wi-Fi routers in residential networks also are DHCP servers that allocate private IPv4 addresses to user devices; they are also network address translation (NAT) gateways. Private IP addresses cannot be routed on the public Internet because they do not uniquely identify the network and its devices.
A NAT-enabled Wi-Fi router has a routable public IP address assigned by an ISP and devices with private IP addresses can share the router’s public IP address to transfer packets to/from other networks.

## Slide 10: Network Layer Technologies
Routers are the predominant Network layer technology. Other important technologies at this layer, include Layer 3 switches, IPsec gateways, and packet filtering firewalls.
A Layer 3 switch is a multilayer switch that combines the functionality of a switch and a router; it can transfer packets between VLANs or subnets and to other networks. Like a router, it can read IP packet headers and make forwarding decisions based on destination IP addresses.
An IPsec gateway is a router that uses IPsec protocols to encrypt IP packet payloads or both the payload and the original IP packet header.
Packet filtering is a firewall technique used to control network access by monitoring outgoing and incoming packets and allowing them to pass or discarding them based on rules applied to IP addresses, Transport and Application layer protocols, and port identifiers.

## Slide 11: TCP/IP’s Data Link Layer
The primary function of the Data Link layer is to move data between hosts in the local network. Physical (MAC) addresses hardcoded in network adapters uniquely identify devices in the local network. These are included in Data Link layer headers and are used by switches or Data Link layer protocols to deliver frames to their destinations.
Other important functions include framing (frames are Data Link layer PDUs, access control (implementing procedures that control how and when devices transmit their data) and error detection (determining whether data is changed in passage between hosts).
The Data Link layer has two sublayers: LLC and MAC that work in concert to perform these communication functions.
In wired Ethernet LANs, Carrier Sense Multiple Access with Collision Detection (CSMA/CD) is the official Data Link layer protocol.
In Wi-Fi LANs, Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA) is the official protocol.
An adapter’s circuitry implements specific Data Link and Physical layer standards (Ethernet or Wi-Fi) and protocols (CSMA/CD or CSMA/CA).

## Slide 12: Data Link Layer Technologies
Network adapters and Layer 2 switches are the most important Data Link layer technologies.
A Layer 2 switch uses physical (MAC) addresses to forward frames within the local network; it is primarily responsible for transferring Data Link layer frames over Physical layer connections in the local network but may also be configured to detect errors. It serves as the central connection point for devices in a wired local network.
In Ethernet LANs, each device connects to a switch via an Ethernet cable. The cable attaches to an interface (port) in the switch. Each switch has a limited number of ports.
A switch’s forwarding table associates each MAC address with the switch port it connect to; when a frame is received, the switch uses the destination MAC address in the header and transmits the frame on the listed port for that MAC address.

## Slide 13: TCP/IP’s Physical Layer
The Data Link layer relies on the Physical layer to transfer data in the local network.
Physical media are the “pipes” that carry the symbols (signals) that represent bits in Data Link layer frames; these should not alter the symbols used to represent bits to enable destination devices to exactly reproduce the frames they are sent.
Data transfer at the Physical Layer requires:
• Physical media (cables or wireless) and associated connectors and interfaces
• The representation of bits on the media (symbols/signals)
• Transmitter and receiver (transceiver) circuitry on adapters
Transmission rate regulation and bit synchronization are other important Physical layer communication functions.
Cables and connectors are important physical layer technologies.

## Slide 14: Physical Layer Technologies
Hubs, repeaters, amplifiers, media converters, modems, and analog-to-digital converters are other Physical layer technologies.
Physically, a hub resembles a switch, but when a hub receives a frame, it retransmits it out of each of its ports.
Repeaters and amplifiers are used to strengthen attenuated signals on communication media.
In enterprise networks, media converters are primarily used to integrate copper and fiber cabling.
A modem (modulator/demodulator) converts (modulates) digital signals to analog signals transmitted on physical media.
Analog-to-digital converters (ADCs) convert analog data/signals to digital signals.

## Slide 15: Summary
Enterprise network infrastructure and communication technologies are important parts of EA’s technical architecture.
Layered communication models including the 7-layer OSI model and the 5-layer TCP/IP model make it easier to understand how device-to-device communication takes place in networks.
Logical connections, data encapsulation, protocols, and addressing enable senders to inform receivers how data should be handled at each layer.
TCP/IP’s Application layer includes both user and service protocols.
TCP/IP’s Transport layer protocols use port addresses support both connection-oriented and connectionless services and applications.
TCP/IP’s Network layer uses IP addresses to identify hosts and transfer packets between devices in different networks.
TCP/IP’s Data Link layer uses Physical (MAC) addresses to transfer data between devices in local networks.
TCP/IP’s Physical layer represents bits as symbols (signal) on physical media and includes cables, connectors, repeaters, media converters, modems, and other important technologies.
All layers of the TCP/IP model are involved in end-to-end, host-to-host communications.