## Slide 1: Key Concepts in Chapter 7
Enterprise Network Infrastructure and Security © Prospect Press Thomas Case

## Slide 2: Data Link and Physical Layer Issues
As Figure 7-2 illustrates, in Wi-Fi networks (802.11 networks), the Data Link layer continues to be responsible for flow framing, physical addressing, error detection, and flow control, but is also responsible for implementing wireless access protocols and reliable data delivery.
Random-access protocols, such as CSMA, can be used, but these must focus on collision avoidance; this makes media access control more complex.
Data delivery is less certain in wireless networks and is affected by transmission range, signal interference, collisions, attenuation, and other factors. To compensate, Wi-Fi frames include sequence numbers to enable receivers to identify missing frames, request retransmission of corrupted frames, and reorder frames into their original transmission sequence.
At the Physical layer, Wi-Fi involves more than representing bits as symbols and signals. Wi-Fi requires frequency band (e.g., 2.4 GHz or 5 GHz) and channel definition, and senders and receivers must be on the same page about the type of signal encoding (waveform modulation).

## Slide 3: Radio Wave Propagation
Electricity flowing through transmitter antennae causes electrons to vibrate and produce radio waves. Radio waves travel through the air and cause receiving antennae to vibrate and produce electric current.
Radio waves occupy a lower frequency range in the electromagnetic spectrum and are separated from the visible light range by the microwave and infrared waves. Ultraviolet light, X-rays, and Gamma rays have higher frequencies than visible light.
Radio waves are analog waveforms with three fundamental characteristics: amplitude, frequency, and phase. Amplitude relates to the height of the wave relative to a zero point; it is often equated with signal strength, with higher amplitudes being stronger signals. Frequency relates to the rate at which the signal repeats; this is measured in cycles per seconds (Hertz.
Phase is how much a signal is shifted with respect to another signal (such as the previous signal) or an ideal or reference signal.

## Slide 4: Carrier Signal Modulation
A carrier signal (aka carrier wave or carrier) is an analog waveform that is modulated (changed) for the purpose of carrying data. It is a base signal that exists on the communication medium when no data is being transferred and is changed (modulated) to represent bits.
Modulation is the process of varying one or more properties of a carrier signal (amplitude, frequency, phase) to represent data.
A modulator is a device that performs modulation. A demodulator is a device that performs demodulation. Demodulation is the inverse of modulation; it enables data to be extracted from the modulated carrier signal. A modem (modulator–demodulator) can perform both modulation and demodulation.

## Slide 5: Multiple Level Modulation
Most modems have multiple-level (M-level) modulation capabilities and routinely transmit analog symbols/signals that represent multiple bits.
With M-level modulation, symbols/signals with more than two amplitudes, frequencies, or phases are transmitted.
For example, when a modem transmits four different amplitudes, each different symbol (amplitude) can represent a two-bit combination (00, 01, 10, 11).
Figure 7-12 illustrates quadrature phase-shift keying (QPSK) which is a type of phase modulation where each transmitted symbol/signal represents two bits; it uses phase shifts (0, 90, 180, or 270 degrees).

## Slide 6: Quadrature Amplitude Modulation (QAM)
Quadrature amplitude modulation (QAM) is a family of modulation methods that combine amplitude and phase modulation to represent bits. QAM is used in Wi-Fi and other wireless networks and in fiber optic communications; members of the QAM family are identified in Table 7-2.
Two carrier waves with the same frequency that are out of phase with one another by 90° are used; this condition is known as quadrature or orthogonality.
M-level amplitude modulation encodes multiple-bit combinations on each carrier wave. The orthogonality of the two carriers enables receivers to coherently separate and demodulate them.
The combination of phase and amplitude shifts for QAM modulation schemes is illustrated by QAM constellation maps. Figure 7-14 illustrates constellation maps for 16 QAM and 64 QAM. Figure 7-15 illustrates the four-bit combination associated with each point in the 16 QAM constellation map.

## Slide 7: Communication Range
Sender-receiver communication is possible when the receiver must be in the sender’s communication range and transmitted signals are strong enough to be accurately detected and decoded.
Receivers located outside a sender’s transmission range that can detect a sender’s weakened signals are in the sender’s detection range. Reliable communication is impossible because the transmitted signal may be too attenuated to be accurately detected and decoded; radio waves in the are detectable by receivers are be unintelligible.
Transmitted signals beyond the detection range are in an interference range. Here, the sender’s signals are severely attenuated and cannot be detected by receivers. However, there may be enough residual strength to contribute background noise and interfere with other signals.
Examples of communication ranges for different types of wireless networks are provided in Table 7-3.
Transmission ranges also contribute to “hidden node” issues in wireless networks. In Figure 7-18, the nodes are “hidden” from each other despite being able to communicate with the access point.

## Slide 8: Wi-Fi Architecture
In the IEEE 802.11 standard, any device with a Wi-Fi adapter a station; the standard also describes the architecture of Wi-Fi networks as having several components, including access points (APs), basic service sets (BSSs), ad-hoc independent basic service sets (IBSSs), and extended service sets (ESSs) that use distribution systems (DSs) to interconnect APs.
A basic service set (BSS) is a wireless network topology that allows stations to communicate through a shared medium called an access point (AP).
Each BSS is uniquely identified by a basic service set identifier (BSSID). Technically, the BSSID is the MAC address of the AP, but a Wi-Fi network typically has a logical name in a list of available networks. The network’s logical name is its service set identifier (SSID).
An extended service set (ESS) consists of two or more BSSs within a logical network segment (such as a subnet or VLAN) and is often described as an interconnected set of BSSs. All APs in an ESS broadcast the same SSID to identify the network; this is called an ESSID. The BSSs in an ESS interconnect via a distribution system (DS).
Specialized switches called Wi-Fi controllers are common in ESSs; a Wi-Fi controller monitors and manages the APs and enables stations to be authenticated, connect to the network, and roam among BSSs.

## Slide 9: Access Point Association
The 802.11 standard identifies carrier sense multiple access with collision avoidance (CSMA/CA) as the official Data Link layer protocol in Wi-Fi networks; CSMA/CA requires a device to associate with an AP prior to using it to transfer data.
Joining a Wi-Fi network is a three-step process: AP discovery, authentication, and association; this is illustrated in Figure 7-24.
Scanning is an important 802.11 part of AP discovery. A Wi-Fi adapter uses scanning to identify an available AP to associate with. Two types of scanning are supported: active and passive. These are described in Table 7-7 and illustrated in Figure 7-25. Mobile devices in new locations often use passive scanning to identify nearby Wi-Fi networks.

## Slide 10: Wi-Fi Media Access Control
CSMA/CA employs two media access controls: the distributed coordination function (DCF) and the point coordination function (PCF). DCF is the Wi-Fi MAC protocol identified in the IEEE 802.11 standard and is officially called CSMA/CA and is illustrated in Figure 7-27.
DCF is contention-based and requires devices to monitor (“sense”) the communication medium before starting to transmit and to refrain from transmitting when the shared medium is being used by another device; DCF uses RTS and CTS frames to avoid data collisions.
PCF works in concert with DCF and is a controlled-access approach that provides hidden nodes an opportunity to transmit. Media access is controlled by the AP. The AP sends poll frames to devices in the BSS that support PCF (not all devices support PCF) and when a device receives the poll, it transmits a frame.
When both PCF and DCF are used, the AP alternates between operating in PCF and DCF modes. Each PCF interval is followed by a DCF interval; this is illustrated in Figure 7-26.

## Slide 11: Evolving Wi-Fi Standards
Revisions (amendments) to the original 802.11 standard have produced successive Wi-Fi generations.
Because the first three generations are considered obsolete, Table 7-8 only considers generations four through seven.
The revisions to the 802.11 standard have brought new capabilities to APs, Wi-Fi adapters, and their antennas; these have contributed to improving Wi-Fi networks.
Taking a closer look at Table 7-8 contents reveals how successive Wi-Fi generations have delivered faster transmission speeds and expanded capabilities.
Table 7-8 identifies several reasons why newer Wi-Fi generations support higher data rates. This includes support for denser QAM constellations, advances in the ability to use multiple-input and multiple-output (MIMO) on Wi-Fi’s shared radio spectrum, OFDM and OFDMA, and the ability to support larger channels are contributing factors

## Slide 12: MIMO & Frequency Bands
Multiple-input and multiple-output (MIMO) is a method for multiplying the capacity of shared radio spectrum by using multiple transmission and receiving antennas.
4 x 4 MIMO has been supported in Wi-Fi networks since Wi-Fi 4. 16 x 16 MIMO is supported in Wi-Fi 7. refers to 16 antennas in transmitters and receivers.
Multi-user MIMO (MU-MIMO) enables an AP to support simultaneous connections with two or more devices.
Since Wi-Fi 4, 802.11 networks have operated in the 2.4 GHz and 5 GHz frequency bands; Wi-Fi 6e and Wi-Fi 7 also use unlicensed space in the 6 GHz frequency band.
5 GHz signals have a shorter wavelength than 2.4 GHz signals and the well-known formula f=1/λ by shows that more waves are sent by higher frequencies (smaller λs) per second than lower frequencies. In Wi-Fi, a modulated 5 GHz carrier can transfer more data per second than a modulated 2.4 GHz carrier.

## Slide 13: Wi-Fi Channel Bonding
The 2.4 GHz and 5 GHz Wi-Fi frequency bands are subdivided into smaller 20 MHz band channels through which data are transferred. The 2.4 GHz band is divided into 14 channels in North America, only channels 1 to 11 are used, and in practice only the non-overlapping channels are used: 1, 6, and 11.
There are 25 20 MHz channels in the 5 GHz frequency band, but in the U.S., the only channels used in mesh networks in buildings are 36, 40, 44, 48, 149, 153, 157, 161, and 165.
According to Shannon’s formula [C=B*log2(1+S/N)], higher bandwidth translates into higher channel capacity. Using channel bonding to create higher bandwidth Wi-Fi channels equates to being able to transfer a higher volume of data through each channel each second.
Channel bonding combines adjacent channels to increase throughput between devices; it has been supported since Wi-Fi 4. Figure 7-34 shows the creation of two nonoverlapping 40 MHz channels by combining adjacent 2.4 GHz channels. 40 MHz, 80 MHz, and 160 MHz nonoverlapping channels can be created in the 5 GHz range.

## Slide 14: OFDM, OFDMA, & WPA3
Orthogonal frequency-division multiplexing (OFDM) is a data transmission method supported since Wi-Fi 2 that subdivides a channel into smaller channels called subcarriers. When an undivided 20 MHz channel is used, each bit in a Wi-Fi frame is transmitted sequentially (serially), one after the other. In OFDM, subcarriers can be used to simultaneously transmit bits (in parallel) and transfer the frame more rapidly.
Orthogonal frequency-division multiple access (OFDMA) enables a channel’s subcarriers to be assigned to different devices. This reduces the need for devices sharing the same channel to have to wait or take turns transmitting data.
With ODFMA, when only one device is connected to the Wi-Fi network, all subcarriers (242) in the channel can be allocated to the device. When there are two users, the channel can be split into two subchannels; four subchannels can support four users, and nine subchannels can simultaneously support nine users.
Wi-Fi security standards and protocols have evolved; today, to be certified by the Wi-Fi Alliance, devices must support WPA2 or WPA3.

## Slide 15: Private 5G RANs
5G New Radio (5G NR) is a physical connection method for radio-based communication that enables wireless interconnections of APs in a 5G radio access network (RAN). 5G NR services have the connection speeds, capacities, and latencies needed to support technologies such as robotics, self-driving vehicles, and ubiquitous IoT devices.
5G has three separate frequency bands; high-band 5G is gaining traction in business facilities to support high-speed, low-latency services and applications.
A private 5G network is a 5G network dedicated to use by a single business or organization, often in a single location such as a factory, hospital, or military base. There are two broad categories of private 5G networks: dependent and independent.

## Slide 16: Summary
Data delivery is less certain in wireless networks than in wired networks and is affected by transmission range, signal interference, collisions, attenuation, and other factors; additional Data Link and Physical layer communication functions are needed.
Radio waves are used in wireless networks to transfer data; carrier signals are modulated to encode data; QAM enables each transmitted signal to represent multiple bits.
BSSs are combined to create ESSs in business facilities; employee devices associate with a BSS AP when joining the network.
BSS APs are shared media and media access protocols enable stations in the BSS to take turns transmitting and receiving data over the shared medium.
CSMA/CA’s DCF is the official Wi-Fi protocol, but PCF can also be used to address hidden node issues.
Wi-Fi continues to evolve; advances in Wi-Fi’s support of QAM, MIMO, channel bonding, OFDM and OFDMA, and WPA3 contribute to improving Wi-Fi network performance and ensuring the likelihood of future use of Wi[Fi in business facilities.
Private 5G RANs are increasingly common in business facilities and have the potential to supplant Wi-Fi for IoT connections and other applications.