## Slide 1: Key Concepts in Chapter 6
Enterprise Network Infrastructure and Security © Prospect Press Thomas Case

## Slide 2: Wired Infrastructure
Although wireless networks are on an upswing, wired infrastructure in business facilities persists and Ethernet continues to evolve to accommodate higher transmission rates required for time-sensitive and bandwidth-intensive applications.
Cabling that supports wired infrastructure in business facilities is usually owned and maintained by the business; it typically supports high transmission speeds and has no recurring costs other than the electricity that powers it.
Structured cabling standards guide the deployment of wired infrastructure in business facilities.
Digital signals are used on almost all wired networks in business facilities and data transmission speeds are usually higher on networks in business facilities than on cabling used to connect locations in business WANs.
To understand the wired LANs that directly support employees and the backbone networks (BNs) that distribute network traffic between and LANs in business facilities, it is necessary to focus on communication functions performed at the Data Link and Physical layers of the TCP/IP model.

## Slide 3: Data Link Layer Functions
The efficiency and reliability of data transfers in the local network stem from several Data Link layer processes identified in Figure 6-1.
Physical (MAC) addresses are used to forward frames between devices in local networks; these are hardwired in network adapters and uniquely identify devices.
Adapters implement the Data Link layer processes identified in Figure 6-1 and described in Table 6-1. Collectively, these processes add efficiency and reliability to data transfers in local networks.
The Data Link layer has two sublayers that work in concert to perform the layer’s communication functions: LLC and MAC. The logical link control (LLC) sublayer manages framing, error detection, and flow control. The media access control (MAC) sublayer manages access control.
MAC headers contain source and destination MAC addresses and control fields. The MAC trailer is used for error checking.

## Slide 4: Access Controls
Media access control is the method used to allocate access to the communication medium and prevent data collisions. There are two parts to media access control: data link control and multiple access control using media access protocols.
Data link control is responsible for reliable transmission over the communication link and involves framing, flow control, and error control; when devices have a dedicated link between them, like they do in a switched Ethernet network, data link control is typically sufficient for reliable data transmission. In the absence of a dedicated link, multiple access control is required to prevent devices from simultaneously trying to seize control of the shared communication channel and transmit.
Multiple access control protocols are used at the MAC sublayer to enable connected devices to access and use a shared communication channel; CSMA/CD and CSMA/CA are examples. These are important in shared media wired networks and in Wi-Fi and other wireless networks; CSMA/CD is toggled off in switched Ethernet networks.

## Slide 5: Error Detection
Prior to the Internet, both error detection and correction functions were usually performed at the Data Link layer. Error detection processes identified frames containing data transmission errors, and error correction processes used ARQ protocols described in Chapter 5.
Frame recipients in local networks can detect errors because frame senders include an error check code in each frame’s MAC trailer field.
Basically, the sender performs a mathematical calculation on the frame’s data and puts the results of its calculation in the trailer field before passing the frame to the Physical layer; the mathematical calculation serves as an error detection value (EDV). The receiver performs the same mathematical calculation on the frame’s data and compares its results to the EDV added by the sender. If the receiver’s EDV matches the sender’s, the receiver concludes that the frame is error-free. If the EDVs are different, the frame is flagged as having errors.
Parity checking, checksums, and cyclic redundancy checking (CRC) are error checking techniques

## Slide 6: Signaling and Line Encoding
Signaling involves the creation of electrical, optical , or wireless signals that represent bits (0s and 1s) on physical media; is the most important Physical layer communication function; the method used to represent bits is called the signaling method.
When fiber optic cabling is used, the signals are light pulses or patterns; in wireless LANs, the signals are radio waveforms.
On copper cables, signaling involves changing the voltage level of an electrical current. As Figure 6-8 illustrates, data can be represented on electronic circuits as analog signals with continuously varying voltage levels or by digital signals with discrete voltage levels. Almost all cabling in business facilities carry digital signals.
A signaling method includes a set of symbols that defines how 1s and 0s are represented on the communication media. A symbol is a transmission medium state or waveform that persists for a specific time duration. Line encoding refers to signaling methods that represent bits as digital signals on communication media.

## Slide 7: Synchronization and Signal Regeneration
Symbol rate, bit rate, and bit interval are important line encoding concepts. In addition to agreement on symbols and symbol rate, a sender and receiver must be synchronized to ensure correct receipt of transmitted signals; bit and frame synchronization techniques help receivers correctly decode transmitted signals.
Bit-level synchronization is usually achieved by providing a clock that controls the sender’s transmission pace and the receiver’s monitoring of the communication link.
When signal attenuation, signal erosion, or synchronization differences are significant, receivers may have difficulty correctly interpreting incoming signals; to compensate, signal regeneration is common in wired networks.
Signal regeneration is a type of signal processing that involves recovering/restoring the signal’s original characteristics, including its symbol shape and timing. Repeaters perform signal regeneration.

## Slide 8: Noise and Errors
In networking, noise is an unwanted disturbance of a transmitted signal; noise is often random rather than persistent. It can come from sources that carry electricity, such as motors, lights, and power cables, and can be created by lightning, and bad connections, and it affects both analog and digital signals.
Figure 6-15 provides an example of how noise can cause transmission errors. Repeaters can clean up much of the signal damage caused by noise, but because all may not be reversed, error detection processes are needed.
Most errors are burst errors. In a burst error, numerous bits are corrupted in clumps by the error-causing condition. A single-bit error happens when only one bit is changed.

## Slide 9: Structured Cabling
Structured cabling refers to building or campus telecommunications infrastructure that consists of multiple standardized elements including network adapters, cable connectors, switch interfaces, and network cabling.
ANSI/TIA-568 structured cabling standards are used to deploy Ethernet LANs and BNs in business facilities; they address the telecommunication subsystems illustrated in Figure 6-16 and described in Table 6-6.
These standards are used to deploy Ethernet LANs and BNs in business facilities in ways that help to avoid signal attenuation, noise, and error-causing conditions.
Twisted-pair cables are the primary type of cable used to connect user equipment to jacks/outlets in work areas and for horizontal cabling between work areas and telecom rooms. Unshielded twisted-pair (UTP) is most common but shielded twisted-pair (STP) may be used to provide additional protection from error sources.

## Slide 10: Fiber Optic Cabling
Optical fiber is the glass (or plastic) portion of a fiber optic cable; it is the light-carrying core of the cable and is surrounded by cladding to keep the light from escaping as it travels through the core.
Single-mode fiber has a smaller core than multimode; its diameter is one-tenth the diameter of a human hair, and its smaller core limits light dispersion and enables signals to be sent over longer distances than multimode.
As light travels through the core in multimode fiber, it bounces off the cladding and when multiple light beams are transmitted at the same time, each beam will have a different path, and the different beams will reach the end of the fiber at different times.
SC, LC, and ST connectors are used on both single-mode and multimode fiber optic cable.

## Slide 11: Ethernet Architecture and Standards
The primary hardware components of an Ethernet LAN are
• Ethernet adapters in client devices, servers, printers, storage equipment, etc.
• Ethernet cables (UTP, STP, fiber optic)
• Ethernet switches
Because Ethernet LANs continue to evolve, there are multiple IEEE standards for Ethernet LANs.
IEEE 802.3 provides an umbrella for the various Ethernet standards that define specifications for Ethernet networks with different transmission speeds.
Some of the best know standards and their associated names and transmission speeds are identified in Table 6-11.
Table 6-12 identifies various physical specifications for Ethernet and their associated media, media standards, and reach (distance).

## Slide 12: 4B/5B Line Encoding
100Base-T (Fast Ethernet) Ethernet uses 4B/5B encoding with NRZI encoding.
4B/5B is a type of block coding that processes groups (blocks) of bits rather than simply creating a symbol/signal for each individual bit.
In 4B/5B, a fifth bit is added to each group of four bits. There are 24 (16) different four-bit groups, and a fifth bit is added to each group to create its corresponding 4B/5B code. Then NRZI encoding is used to represent 4B/5B codes on the Ethernet cable. Receivers convert the 4B/5B code back to the original four bits.
Similar types of block coding are used in higher speed Ethernet LANs. For example, 8B/10B is used in Gigabit Ethernet LANs.

## Slide 13: Power Over Ethernet
Power over Ethernet (PoE) refers to standards and technologies that enable both electric power and data signals to be carried on twisted-pair Ethernet cables; with PoE, network devices do not need a separate power supply or power cord and PoE is widely used to power access points in Wi-Fi LANs, IP security/surveillance cameras, and other devices.
PoE standards address several different power and voltage levels; there are 60W and 100W versions of PoE++. Generally, higher power and voltage levels enable a wider range of devices to be powered.
Today, Ethernet switches that do not support PoE are rare. However, PoE midspans can be added to non-PoE switches to provide power to devices.

## Slide 14: Backbone Networks
In networking, a backbone is network infrastructure that interconnects different networks and provides a pathway for them to exchange data.
A backbone network (BN) can connect different networks in the same building or networks in different buildings in a campus environment; a BN may also connect networks at geographically distributed locations.
Best practices for BNs include having at least two, but not more than three, layers of switches. This conforms to the three-layer hierarchical model.
There are two major backbone network architectures: routed and switched. A routed backbone uses IP addresses and routers to forward packets; the network’s IP space is divided into subnets. A switched backbone network typically conforms to the three layer-hierarchical model.

## Slide 15: Network Resilience and Wired Network Security
Network resilience is the degree to which a network can quickly recover from network disruptions and maintain services when disruptions occur. Circuit redundancy can be used at all layers of the three-layer hierarchical model to improve resilience.
Redundant power supplies, backup generators, and redundant links to internal and external electrical grids contribute to network resilience. So do readily available spare plug-and-play (PnP)networking equipment to replace failed counterparts.
Protecting wired networks begins with controlling access to telecommunication rooms, equipment rooms, data centers, and other spaces that contain critical network infrastructure.
Network cable conduit and cable trays can keep network cabling out of harm’s way and increase its security.

## Slide 16: Summary
Wired LANs and BNs remain common in business facilities and their communications map to TCP/IP’s Data Link and Physical layers.
Framing, access control, data link control, and error detection are important Data Link layer communication functions.
Data Link layer frames include destination and sender MAC addresses; MAC addresses are hardcoded in adapters and used by Layer 2 switches to forward frames to destinations.
Signaling is the most important Physical layer communication function; digital signals and line encoding is used on LAN and BN cables in business facilities.
Repeaters are used to recover attenuated and eroded signals on cables and error detection processes are used to address corrupted signals.
Structured cabling standards provide guidance for deploying wired LANs and BNs in business facilities.
UTP is the most common type of copper cable, but STP is used in noisy environments.
Both single-mode and multimode fiber optic cable may be used in business facilities, but multimode is most common.
Most wired LANs and BNs in business facilities are Ethernet networks that use 4B/5B-family encoding schemes; PoE is increasingly common.
Routed, switched and hybrid BNs are used in enterprise networks.
Redundant circuits and components contribute to network resilience; restricting access to wired infrastructure contributes to its security.