## Slide 1: Key Concepts in Chapter 9
Enterprise Network Infrastructure and Security © Prospect Press Thomas Case

## Slide 2: Business and the IoT
The IoT is one of the most important and disruptive technologies of the twenty-first century.
Businesses are changing their networks to accommodate IoT connections and data, and multiple industries already have more than 100 million connected IoT devices.
The total number of IoT devices across all industries in 2030 is expected to exceed 8 billion. Figure 9-1 summarizes the installed base of IoT devices from 2019 until now and identifies IoT’s expected growth through 2030. Advances in several areas contribute to this growth.
Low-cost and energy-efficient (low-power) sensor technologies.
IoT-oriented network protocols
IoT-friendly networks such as low-power wide area network (LPWAN),
Cloud computing platforms that provide processing and storage infrastructure for IoT scalability and management.
Analytics that enable insights into IoT data rapidly and easily.
Conversational AI and natural-language processing (NLP) for human-to-device communications.
Machine learning (ML) and AI algorithms that enable autonomous, self-managing, and ever-smarter systems and processes.

## Slide 3: Business Process Enhancements
Many businesses are deploying IoT devices and systems to enhance existing processes, including manufacturing, supply chains, asset management, and employee health and safety, often without having to reengineer the processes.
The IoT is also being used to improve warehouse and inventory management, IT and network management and security, customer service, and financial services.
The Industrial Internet of Things (IIoT) refers to interconnected sensors, devices, networking infrastructure, and applications that work together to monitor, collect, and analyze data from industrial operations.
Applying advanced analytics to IIoT data helps to:
Increase the productivity, uptime, and overall effectiveness of manufacturing equipment and facilities
Improve the efficiencies of manufacturing processes
Create end-to-end operational visibility
Improve product quality
Reduce operating costs
Optimize production scheduling
Accelerate innovation

## Slide 4: SCADA and the IIoT
IIoT networks include traditional manufacturing systems such as SCADA.
Supervisory control and data acquisition (SCADA) software applications control industrial equipment and processes using real-time data. Like IIoT systems, systems include sensors and actuators that monitor/measure the status of industrial equipment and control how the equipment operates. But there are differences and IIoT applications extend beyond manufacturing to
Some businesses are using the IoT to manage, secure, and improve the performance of their networks.

## Slide 5: Industry 4.0 & Warehouse 4.0
Industry 4.0 refers to the integration of intelligent digital technologies into manufacturing and industrial processes. It consists of numerous converging technologies including IIoT networks, AI, Big Data, robotics, and additive manufacturing. Industry 4.0 is a new phase in the Industrial Revolution that facilitates smart manufacturing and the creation of intelligent factories.
Integrated supply chains and Warehouse 4.0 enable Industry 4.0 manufacturing facilities to achieve performance levels beyond what they can reach on their own.
Warehouse 4.0 (W4.0) leverages the IoT, Big Data and data science, augmented reality, wearables, computer vision, artificial intelligence, sensors, collaborative robots (cobots), robots, and other technologies to enable warehouses to be “smart” components of integrated supply chains. It strives to facilitate materials management in warehouses, drive efficiencies, reduce costs, and improve overall warehouse management.

## Slide 6: V2V Communication
Vehicle-to-vehicle (V2V) communication is often considered an articulation of machine-to-machine (M2M) communication at the intersection of the IoT and intelligent transportation system (ITS) initiatives; ITS overlaps with smart logistics, smart fleet management, connected cars, and smart cities. V2V communication enables vehicles to wirelessly exchange information about their speed, location, and direction.
Vehicles equipped with appropriate sensors, software, systems, and safety applications can use messages from surrounding vehicles to identify potential collision threats in real time so that they can take actions needed to avoid crashes.
V2V communication is an aspect of vehicle-to-everything (V2X) communication. Vehicle-to-everything (V2X) communication is communication between a vehicle and any entity that may affect or be affected by the vehicle; it includes:
vehicle-to-infrastructure (V2I),
vehicle-to-network (V2N), and
vehicle-to-pedestrian (V2P) communication.

## Slide 7: Digital Business, Transformation, & Twins
Digital business creates new business models and revenue streams from new combinations of people, technology, and business processes; like the IoT, digital business encompasses the convergence of digital and physical worlds and involves leveraging technologies to support their core operations, create new capabilities, and improve customer and employee engagement.
Digital business is considered an offshoot of digital transformation—the adoption and use of digital technologies to transform services or products and the replacement of manual processes with digital processes and the replacement of older digital technologies with newer ones. Basically, digital transformation is the integration of digital technology into all facets of business and fundamentally changing how businesses operate and deliver value to customers.
A digital twin is a virtual representation of a physical object or process that serves as a real-time digital counterpart for the object or process. Essentially, a digital twin is implemented as a software object (computer program) or model that mirrors the physical object or process and can be used in simulations for learning/predicting how the object or process might perform in different conditions or to identify ways it might be improved.

## Slide 8: IoT Architectures & Platforms
Online research on IoT architectures can reveal several varieties that from three eight layers.
The seven-layer IoT reference model developed by the IoT World Forum is the best known.
An IoT platform is a cloud or on-premises software suite that monitors, manages, and controls IoT networks, endpoints, and applications.
IoT platforms facilitate device/endpoint management, connectivity and network management, data accumulation, data management, data processing and analysis, and application development. IoT platforms can also have important roles in securing IoT networks and applications.
Basically, IoT platforms include software that enables all layers of IoT architectures to work together to achieve business goals.

## Slide 9: IoT Device Capabilities
According to the Industrial IoT Consortium, devices in IIoT networks should have transducing, data, and interface capabilities; these are directly related to device functionality.
Transducing capabilities enable the device to interact with the physical world; they provide connections between the device’s digital and physical environments.
A device’s data capabilities (storage, processing, transfer) enable it to provide inputs into other IT systems, including IoT platforms and applications.
Its interface capabilities enable it to interact with other IoT components (including networks and human users).
In IoT contexts, a sensor is an electrical instrument that monitors and measures physical aspects of an environment; it provides an observation of an aspect of the physical world in the form of measurement data.
In an IoT device, an actuator receives electrical signals from an IoT controller and turns them into physical outputs or actions; they make a change in the physical world based on inputs they receive.

## Slide 10: IoT Gateways and Protocols
An IoT gateway enables a connection between IoT devices at the physical (perception) layer and device-to-cloud communication over the Internet or another communication network.
An IoT gateway links IoT devices to the Internet/cloud or to private networks/WANs; it does this by converting IoT device data into formats needed to support a variety of specialized protocols used in IoT networks.
Private 5G RANs are increasingly being used for wireless communications in factories and warehouses. Most IIoT device deployments are expected to connect to 5G RANs in the years ahead.

## Slide 11: Edge Computing, Data Accumulation, and Data Abstraction
Edge computing is a distributed IT architecture that involves processing data at the periphery of a communications network as close as possible to the originating data source. Doing this saves time and resources needed to send all data to cloud services. Edge computing is a standard practice in 5G networks that support IoT systems and applications.
Edge computing occurs at gateways, local servers, or other edge devices. Edge devices have enough memory and processing power to collect, process, and use data from nearby data sources (in close to real time) with limited or no help from technologies in other parts of the network.
Activities at the Data Accumulation layer are usually performed by IoT platforms. Data accumulation involves storing real-time data from edge and physical devices to meet the requirements of non–real-time applications.
IoT platforms also oversee data abstraction activities. At the Data Abstraction layer, data preparation is finalized for IoT applications; it also reformats data from the applications layer to ensure that it is in a form that physical layer devices can understand. Essentially, it prepares data for use by IoT applications and prepares data from applications for use by devices.

## Slide 12: The IoT Reference Model’s Applications and Collaboration and Processes Layers
At the Applications layer, IoT data is analyzed by software to inform decision-making and provide answers to business questions. Many IoT platforms include application development and maintenance capabilities; they may include ready-to-use or easily customizable data mining, data visualization, and analytics tools.
Examples of IoT applications include:
• Device monitoring and control systems
• Mobile apps for simple interactions with IoT devices/systems
• Cloud-based BI services
• Analytic solutions using ML
At the Collaboration and Processes layer, application results are provided to users, business owners, and stakeholders; the results, and the data/information on which they are based, add value when they facilitate problem-solving and the achievement of business goals.
A challenge at this layer is effectively leveraging the growing volume and value of IoT data/information for business optimization and economic growth.

## Slide 13: IoT Network Security
With accelerating IoT adoption and use, IoT networking is an important business issue, and businesses are coming to grips with IoT security; devices, communication channels, and applications may be attacked.
Often, security focuses on hardening IoT systems against data breaches, malicious software, and hacking; cloud security mechanisms are common parts of IoT infrastructure security.
Many businesses have adopted SD-WANs to segregate and secure the data flows generated and consumed by IoT devices, gateways, platforms, and applications.

## Slide 14: Summary
Enterprise networks increasingly support IoT systems and applications.
IoT devices and applications are being used to support and improve processes in a wide range of industries.
Industrial IoT, Industry 4.0, and Warehouse 4.0 applications facilitate the creation of smart factories, warehouses, and supply chains and are important contributors to the digital transportation of business.
V2V and V2X communications are important aspects of self-driving vehicles on roads and within business facilities.
The 7-layer IoT reference model from the IoT World Forum exemplifies IoT architecture models.
IoT platforms enable all layers of IoT architectures to work together to achieve business goals.
IoT devices have transducing, data, and interface capabilities; sensors and actuators perform transducing tasks.
Edge computing is common in IoT networks and is performed by IoT gateways and other edge devices.
IoT systems and applications add vulnerabilities to enterprise networks.
SD-WAN is increasingly used to manage and secure IoT applications.